ACT AIR QUALITY REPORT 2009

Environment Protection Authority | June 2010

# CONTENTS

CONTENTS	2

LIST OF TABLES	3

LIST OF FIGURES	4

OVERVIEW	5

ACT’s air quality	5

Current Performance Monitoring Stations	5

Emissions (sources of pollution)	6

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL	8

Carbon monoxide	9

Nitrogen dioxide	11

Ozone	12

PM10	15

PM2.5	16

ANALYSIS OF AIR QUALITY MONITORING	17

Carbon monoxide	17

Nitrogen dioxide	17

Ozone	18

PM10	18

PM2.5	19

ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL	20

APPENDIX A: STATISTICAL SUMMARY AND TRENDS	21

Carbon monoxide	21

Nitrogen dioxide	23

Ozone	26

PM10	30

PM2.5	32

# LIST OF TABLES

Table 1: NEPM standards and goals	8

Table 2: 2009 compliance summary for CO	9

Table 3: 2009 compliance summary for NO2	11

Table 4: 2009 compliance summary for O3	12

Table 5: 2009 compliance summary for PM10	15

Table 6: 2009 compliance summary for PM2.5	16

Table 7: 2009 summary statistics for daily peak 8-hour CO	17

Table 8: 2009 summary statistics for daily peak 1-hour NO2	17

Table 9: 2009 summary statistics for daily peak 1-hour O3	18

Table 10: 2009 summary statistics for daily peak 4-hour O3	18

Table 11: 2009 summary statistics for daily peak PM10	18

Table 12: 2009 summary statistics for daily peak PM2.5	19

Table 13: Statistical summary for daily maximum 8-hour CO Monash 1999 – 2009	21

Table 14: Statistical summary for daily maximum 8-hour CO Civic 1999 – 2009	22

Table 15: Statistical summary for daily maximum 1-hour NO2 Monash 1999 – 2009	23

Table 16: Statistical summary for daily maximum 1-hour NO2 Civic 1999 – 2009	24

Table 17: Statistical summary for daily maximum 1-hour O3 Monash 1999 – 2009	26

Table 18: Statistical summary for daily maximum 1-hour O3 Civic 1999 – 2009	27

Table 19: Statistical summary for daily maximum 4-hour O3 Monash 1999 – 2009	28

Table 20: Statistical summary for daily maximum 4-hour O3 Civic 1999 – 2009	29

Table 21: Statistical summary for daily maximum 24-hour PM10 Monash 1999 – 2009	30

Table 22: Statistical summary for daily maximum 24-hour PM10 Civic 1999 – 2008	31

Table 23: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2009	32

# LIST OF FIGURES

Figure 1: Sources of oxides of nitrogen	6

Figure 2: Sources of carbon monoxide	7

Figure 3: Sources of particulate matter PM10	7

Figure 4: Daily max for CO 8-hr average – Monash	10

Figure 5: Daily max for CO 8-hr average – Civic	10

Figure 6: Daily max for NO2 – Monash	11

Figure 7: Daily max for NO2 – Civic	12

Figure 8: Daily max for 1 hour O3 – Monash	13

Figure 9: Daily max for 1 hour O3 – Civic	13

Figure 10: Daily max for 4 hour O3 – Monash	14

Figure 11: Daily max for 4 hour O3 – Civic	14

Figure 12: Daily max for PM10 – Monash	15

Figure 13: Daily max for PM2.5 – Monash	16

Figure 14: Statistical summary for daily maximum 8-hour CO Monash 1999 – 2009	21

Figure 15: Statistical summary for daily maximum 8-hour CO Civic 1999 – 2009	22

Figure 16: Statistical summary for daily maximum 1-hour NO2 Monash 1999 – 2009	23

Figure 17: Statistical summary for daily maximum 1-hour NO2 Civic1999 – 2009	24

Figure 18: Annual average 1-hour NO2 Monash 1999 – 2009	25

Figure 19: Annual average 1-hour NO2 Civic 1999 – 2009	25

Figure 20: Statistical summary for daily maximum 1-hour O3 Monash 1999 – 2009	26

Figure 21: Statistical summary for daily maximum 1-hour O3 Civic 1999 – 2009	27

Figure 22: Statistical summary for daily maximum 4-hour O3 Monash 1999 – 2009	28

Figure 23: Statistical summary for daily maximum 4-hour O3 Civic 1999 – 2009	29

Figure 24: Statistical summary for daily maximum 24-hour PM10 Monash 1999 – 2009	30

Figure 25: Statistical summary for daily maximum 24-hour PM10 Civic 1999 – 2008	31

Figure 26: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2009 ...32 Figure 27: Annual average 24-hour PM2.5 Monash 2004 – 2009	33

# OVERVIEW

## ACT’s air quality

This report presents the results of air quality monitoring in the ACT and assesses them against the requirements of the Ambient Air Quality National Environment Protection Measure (the NEPM).

Canberra’s overall air quality compared to other capital cities is excellent. However it does experience elevated particle pollution during winter due to emissions from domestic wood heaters. The ACT Government acknowledges the problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

Consistent with the reporting period defined in the NEPM this report covers a calendar year ending on 31 December 2009.

The major impacts on Canberra’s air quality in 2009, as in previous years, came from the accumulation of combustion particles from wood heaters in cold, highly stable air and dust storms. With the exception of particulate matter all measured parameters are below NEPM standards.

## Current Performance Monitoring Stations

The ACT Government has been undertaking ambient air quality monitoring in Canberra since the early 1990’s. ACT Health is responsible for the Government’s ambient air quality monitoring network, which currently consists of two performance monitoring stations  (PMS).

The ACTs population has passed the threshold where it needs a second NEPM PMS. Previous annual reports have been based solely on data from the PMS at Monash.

Although not ideally located for national reporting purposes, data from the PMS at Civic will be used for annual report purposes pending the establishment of another NEPM PMS by ACT Health.

The Civic PMS is located at the northern end of the carpark on the western side of the olympic swimming pool adjacent to Allara Street. The Monash PMS is approximately 300 metres west of Cockcroft Avenue in the Monash district playing fields.

Consistent with the ACT’s Ambient Air Quality Monitoring Plan, which was approved by the National Environment Protection Council in 2001, this report only covers four of the six criteria pollutants, namely carbon monoxide (CO), nitrogen dioxide (NO2), photochemical oxidants as ozone (O3) and particulate matter less than 10 micrometres (PM10). Due to a lack of heavy industry the ACT has never monitored sulphur dioxide, and ceased monitoring lead in July 2002, following the phase out of leaded fuel on 1 January 2002,  with ambient air lead levels being less than 2% of the standard. The report also covers particulate matter less than 2.5 micrometres (PM2.5).

Both stations contain instrumentation that continuously monitors CO, O3, NO2. Particulate matter less than 10 and 2.5 micrometres (microns) in diameter – known as PM10 and PM2.5 respectively – are only measured at Monash (to put the size of these particles into perspective the average human hair is 60 – 100 microns in diameter).

## Emissions (sources of pollution)

Air pollutant emissions in Canberra are dominated by motor vehicles, with the exception of particulate matter which increase during winter due to emissions from wood heaters.

The following charts are based on 2008/2009 National Pollution Inventory (NPI) data and show the main sources of emissions for oxides of nitrogen, carbon monoxide and particulate matter for Canberra. (http://www.npi.gov.au/overview/reports/act-location- report.html).

No emissions data is presented for ozone as this is a secondary pollutant, formed by the reactions of other primary pollutants. It is not directly emitted from a particular source and therefore is not reported under the NPI.

Figure 1: Sources of oxides of nitrogen

Figure 2: Sources of carbon monoxide

3%	2%

5%

8%

10%

72%

Figure 3: Sources of particulate matter PM10

# ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL

For the purpose of this report air quality is assessed against the NEPM standards and goals as specified in Schedule 2 of the NEPM and reproduced below in Table 1. The NEPM was made in June 1998.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3, Table 1).

The goal of the NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specified in Schedule 2 of the NEPM. The extent is expressed as a maximum allowable number of exceedences for each standard (refer to column 4, Table 1). These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfires, that cannot be controlled through normal air quality management programs.

The NEPM also specifies advisory reporting standards for PM2.5. The goal for PM2.5 is to collect sufficient data to facilitate a review of the PM2.5 standards. This review is currently being undertaken as part of the broader NEPM review.

Table 1: NEPM standards and goals

| Pollutant | Averaging Period | Maximum concentration | Goal within 10 years Maximum allowable exceedences |
| --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year none |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year none |
| Lead | 1 year | 0.050 µg/m3 | none |
| Particles as PM10 | 1 day | 50 µg/m3 | 5 days a year |
| Particles as PM2. # 5 | 1 day 1 year | 25 µg/m3 8 µg/m3 | Gather sufficient data nationally to facilitate a review of Advisory Reporting Standard. |

# - Reporting standard only

The following tables summarise compliance with the standards and goals of the NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded, the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

Air quality is assessed as complying with the NEPM if the number of exceedences of the standard is no more than the number specified in Schedule 2 of the NEPM and data availability was at least 75 per cent in each quarter of the year. Air quality is assessed as ‘not demonstrated’ if there has been insufficient data collected to demonstrate that the standards and goal have been met or not met.

## Carbon monoxide

During 2009, no exceedences of the CO standard were recorded in the ACT. Levels are well below the NEPM standard and because of both an improvement in vehicle emissions and a decline in wood heaters numbers, levels are trending down (refer Figure 14 and 15). The highest recorded value in the ACT during 2009, was 2.0 ppm at Monash. This is only 22% of the standard.

Table 2: 2009 compliance summary for CO NEPM standard - 9.0 ppm (8-hr average)

The following time series graphs (Figure 4 to Figure 13) enable a quick visual comparison to the NEPM standards for the 2009 reporting period. The figures show, with the exception of particulate matter, all levels are below the standards.

Monash

10

9

8

7

6

5

4

3

2

1

0

Figure 4: Daily max for CO 8-hr average – Monash.

10.0

Civic

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

Figure 5: Daily max for CO 8-hr average – Civic.

## Nitrogen dioxide

During 2009, no exceedences of the NO2 standard were recorded in the ACT. Monash complied with both the 1 hour average and 1 year average goals for nitrogen dioxide.

Compliance was not demonstrated for Civic because insufficient data was available for the first quarter of the year (Refer Table 3 and Figure 4).

NO2 levels are well below the NEPM standard and have remained stable over the last decade. The highest recorded 1 hour value during 2009 was 0.043 ppm at Civic. This is only 36% of the standard. The highest recorded annual average in 2009, was 0.008ppm at Civic. This is only 26% of the standard.

Table 3: 2009 compliance summary for NO2

NEPM standard – 0.12 ppm (1 hour average), 0.03 ppm (1 year average)

| Region/ Performance monitoring station | Data availability rates (% of hours) | Annual mean Concentration (ppm) | Number of 1 hour exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 hour | 1 year |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |  |  |
| Canberra Monash Civic | 95.8 52.9 | 94.3 75.0 | 90.3 95.6 | 94.2 90.0 | 93.7 78.5 | 0.006 0.008 | 0 0 | Met ND | Met ND |

0.14

Monash

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 6: Daily max for NO2 – Monash.

0.14

Civic

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 7: Daily max for NO2 – Civic.

## Ozone

During 2009, no exceedences of the 1 hour and 4 hour standard for O3 were recorded in the ACT. Levels are below the NEPM standard and appear to have increased slightly over the last decade at Monash (refer Figure 20). The highest recorded 1-hour value in the ACT during 2009, was 0.073 ppm at Monash. This is 73% of the standard. The highest recorded 4-hour value in the ACT during 2009, was 0.068 ppm at Monash. This is 85% of the standard.

Table 4: 2009 compliance summary for O3

NEPM standard – 0 10 ppm (1 hour average), 0.08 ppm (4 hour average)

| Region/ Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Canberra | 90.5 | 95.5 | 91.4 | 95.5 | 93.2 | 0 | 0 | Met | Met |
| Monash |  |  |  |  |  |  |  |  |  |
| Civic | 95.7 | 95.6 | 94.5 | 92.2 | 94.5 | 0 | 0 | Met | Met |

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 8: Daily max for 1 hour O3 – Monash.

0.12

Civic

0.1

0.08

0.06

0.04

0.02

0

Figure 9: Daily max for 1 hour O3 – Civic.

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

Figure 10: Daily max for 4 hour O3 – Monash.

0.09

Civic

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

Figure 11: Daily max for 4 hour O3 – Civic.

PM10

During 2009, compliance with the NEPM goal was not met because nine exceedences of the 24-hr PM10 standard were recorded at Monash. Data was also not available for the period 1 January to 8 June because of instrument failure.

Table 5: 2009 compliance summary for PM10 NEPM standard 50 g/m3 1 day average

The highest PM10 level recorded during 2009, was 210 µg/m3 on 22 September when most of eastern Australia was covered in red dust after an extreme low pressure system moved across from central Australia. This is 420% of the NEPM standard.

As with previous years, exceedences continue to be caused by wood heater emissions during extremely cold and stable atmospheric conditions and natural events such as dust storms. Excluding these climatological effects, PM10 levels have been falling in the Tuggeranong Valley (refer Figure 24).

250

Monash

200

150

100

50

0

Figure 12: Daily max for PM10 – Monash.

PM2.5

During 2009, two exceedences of the 24-hr advisory reporting standard were recorded at Monash. Data was not available for the period 1 January to 23 February, 5 to 26 May and 4 to 24 June because of instrument failure.

Table 6: 2009 compliance summary for PM2.5   NEPM standard – 25 g/m3 (1 day), 8 g/m3 (1year)

Monash

40

35

30

25

20

15

10

5

0

Figure 13: Daily max for PM2.5 – Monash.

# ANALYSIS OF AIR QUALITY MONITORING

Annual summary statistics described in Tables 7 to 12 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The NEPM states that the short-term standards should not be exceeded on more than one day for CO, NO2, O3, SO2 and on no more than five days per year for PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

## Carbon monoxide

Table 7: 2009 summary statistics for daily peak 8-hour CO NEPM standard - 9.0 ppm (8-hr average)

## Nitrogen dioxide

Table 8: 2009 summary statistics for daily peak 1-hour NO2 NEPM standard 0.12 ppm (1 hour average)

## Ozone

Table 9: 2009 summary statistics for daily peak 1-hour O3 NEPM standard 0.10 ppm (1-hour average)

Table 10: 2009 summary statistics for daily peak 4-hour O3 NEPM standard 0.08 ppm (4-hour average)

PM10

Table 11: 2009 summary statistics for daily peak PM10 NEPM standard 50 g/m3 (24-hour average)

PM2.5

Table 12: 2009 summary statistics for daily peak PM2.5 NEPM standard 25 g/m3 (24-hour average)

# ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL

The ACT is making steady progress towards achieving the goal of the NEPM, which is to achieve the standards specified in Schedule 2.

Historical monitoring indicates that the only NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions coming from domestic wood heaters. In more recent years exceedences of the particulate matter standard have also been recorded from dust storms and bushfire smoke because of continuing drought conditions in the region.

Monitoring in 2009 showed that the NEPM goal and standards were met for carbon monoxide, nitrogen dioxide and ozone at Civic and Monash.

The goal was not met for PM10, with nine exceedences of the standard recorded at Monash. Four could be attributed to woodsmoke as they occurred during the traditional wood heating season. The remainder are due to dust storms, including the extreme event which occurred on 22 and 23 September when most of eastern Australia was covered in red dust after an extreme low pressure system moved across from central Australia.

The 24-hour advisory reporting standard for particles (as PM2.5 ) was exceeded on two occasions at Monash. It should be noted however that significant gaps occurred in the PM10 and PM2.5 data sets when levels would be expected to be elevated from woodsmoke.

The Monash station was closed for relocation on 26 October 2008. Due to equipment failure and on-going calibration problems in re-establishing the station PM10 monitoring did not recommence until 9 June 2009. Similarly, PM2.5 monitoring ceased at Monash on 9 August 2008 and did not recommence until 24 February 2009. Data is also missing for most of May and June.

PM10 monitoring ceased in Civic on 8 December 2008. ACT Health is currently installing a continuous PM10 monitoring instrument and it is envisaged that monitoring will recommence this winter.

The ACT Government acknowledges the woodsmoke problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

The Department of the Environment, Climate Change, Energy and Water continues to implement its integrated program to address wood smoke. This involves public education and enforcement activities, the licensing of firewood merchants, the implementation of the ‘Don’t Burn Tonight Campaign’ and the Wood Heater Replacement Program.

The ACT is also working with the Commonwealth and other jurisdictions through the Air Quality Working Group of the Environment Protection and Heritage Council on national approaches to reduce particle and ozone precursor emissions from the product and equipment sectors, including from wood heaters, small engines, surface coatings

and non-road engines.

# APPENDIX A: STATISTICAL SUMMARY AND TRENDS

The following section provides a basic statistical summary, using percentiles, for each station and for each standard. Percentiles for daily maximum values are presented.

## Carbon monoxide

Table 13: Statistical summary for daily maximum 8-hour CO Monash 1999 – 2009

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 82.6 | 0 | 4.5 | 4.2 | 4.2 | 3.7 | 3.2 | 2.2 | 0.7 |
| 2000 | 79.1 | 0 | 5.8 | 4.5 | 4.4 | 3.7 | 3.0 | 1.7 | 0.7 |
| 2001 | 91.7 | 0 | 4.2 | 4.0 | 3.8 | 3.1 | 2.5 | 1.2 | 0.4 |
| 2002 | 92 | 0 | 4.3 | 3.7 | 3.4 | 2.9 | 2.3 | 1.2 | 0.4 |
| 2003 | 86.8 | 0 | 3.7 | 3.0 | 2.8 | 2.5 | 2.0 | 0.8 | 0.3 |
| 2004 | 94.1 | 0 | 3.2 | 2.7 | 2.5 | 2.0 | 1.6 | 0.9 | 0.5 |
| 2005 | 99.5 | 0 | 3.2 | 2.8 | 2.5 | 2.2 | 1.7 | 1.0 | 0.4 |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 14: Statistical summary for daily maximum 8-hour CO Monash 1999 – 2009

Table 14: Statistical summary for daily maximum 8-hour CO Civic 1999 – 2009

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 83.2 | 0 | 7.5 | 6.6 | 6.2 | 5.5 | 4.9 | 3.1 | 1.5 |
| 2000 | 91.7 | 0 | 6.3 | 5.9 | 5.6 | 4.8 | 3.3 | 1.8 | 1.0 |
| 2001 | 83.2 | 0 | 6.4 | 5.6 | 4.8 | 4.0 | 3.2 | 2.1 | 1.0 |
| 2002 | 86.8 | 0 | 5.1 | 4.7 | 4.4 | 3.52 | 2.9 | 1.6 | 0.6 |
| 2003 | 95.7 | 0 | 3.5 | 2.8 | 2.6 | 2.2 | 1.8 | 1.0 | 0.6 |
| 2004 | 95.7 | 0 | 4.6 | 3.6 | 3.2 | 2.3 | 1.6 | 0.6 | 0.6 |
| 2005 | 95.6 | 0 | 3.7 | 3.4 | 3.2 | 2.6 | 1.7 | 1.1 | 0.7 |
| 2006 | 95.4 | 0 | 2.8 | 2.7 | 2.6 | 2.1 | 1.4 | 0.8 | 0.5 |
| 2007 | 93.2 | 0 | 2.8 | 2.3 | 2.0 | 1.6 | 1.3 | 0.8 | 0.5 |
| 2008 | 92.7 | 0 | 2.3 | 2.1 | 2.0 | 1.6 | 1.2 | 0.7 | 0.4 |
| 2009 | 95.1 | 0 | 1.9 | 1.6 | 1.2 | 1.0 | 0.8 | 0.6 | 0.4 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 15: Statistical summary for daily maximum 8-hour CO Civic 1999 – 2009

## Nitrogen dioxide

Table 15: Statistical summary for daily maximum 1-hour NO2 Monash 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 86.3 | 0 | 0.054 | 0.034 | 0.031 | 0.030 | 0.028 | 0.025 | 0.019 |
| 2000 | 90.0 | 0 | 0.042 | 0.034 | 0.031 | 0.028 | 0.026 | 0.022 | 0.018 |
| 2001 | 86.3 | 0 | 0.039 | 0.036 | 0.036 | 0.033 | 0.029 | 0.024 | 0.020 |
| 2002 | 88.3 | 0 | 0.045 | 0.036 | 0.034 | 0.031 | 0.026 | 0.022 | 0.017 |
| 2003 | 90.4 | 0 | 0.064 | 0.042 | 0.033 | 0.028 | 0.025 | 0.021 | 0.016 |
| 2004 | 91.8 | 0 | 0.040 | 0.033 | 0.031 | 0.028 | 0.026 | 0.022 | 0.018 |
| 2005 | 97.8 | 0 | 0.041 | 0.034 | 0.031 | 0.028 | 0.027 | 0.024 | 0.018 |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 16: Statistical summary for daily maximum 1-hour NO2 Monash 1999 – 2009

Table 16: Statistical summary for daily maximum 1-hour NO2 Civic 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 61.6 | 0 | 0.054 | 0.040 | 0.037 | 0.035 | 0.032 | 0.029 | 0.023 |
| 2000 | 55.6 | 0 | 0.055 | 0.039 | 0.038 | 0.034 | 0.032 | 0.028 | 0.025 |
| 2001 | 87.0 | 0 | 0.048 | 0.045 | 0.042 | 0.039 | 0.037 | 0.032 | 0.027 |
| 2002 | 88.2 | 0 | 0.062 | 0.050 | 0.044 | 0.038 | 0.034 | 0.029 | 0.024 |
| 2003 | 83.6 | 0 | 0.087 | 0.050 | 0.045 | 0.034 | 0.028 | 0.022 | 0.018 |
| 2004 | 88.3 | 0 | 0.042 | 0.037 | 0.035 | 0.030 | 0.027 | 0.022 | 0.018 |
| 2005 | 95.3 | 0 | 0.040 | 0.036 | 0.033 | 0.030 | 0.029 | 0.024 | 0.020 |
| 2006 | 95.2 | 0 | 0.044 | 0.035 | 0.034 | 0.031 | 0.028 | 0.022 | 0.018 |
| 2007 | 92.8 | 0 | 0.059 | 0.042 | 0.039 | 0.035 | 0.030 | 0.025 | 0.021 |
| 2008 | 88.6 | 0 | 0.046 | 0.037 | 0.035 | 0.033 | 0.030 | 0.026 | 0.020 |
| 2009 | 79.5 | 0 | 0.044 | 0.038 | 0.036 | 0.030 | 0.027 | 0.023 | 0.018 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 17: Statistical summary for daily maximum 1-hour NO2 Civic1999 – 2009

0.035

0.025

0.02

0.015

0.01

0.005

0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 18: Annual average 1-hour NO2 Monash 1999 – 2009

0.035

0.03

0.025

0.02

0.015

0.01

0.005

0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 19: Annual average 1-hour NO2 Civic 1999 – 2009

## Ozone

Table 17: Statistical summary for daily maximum 1-hour O3 Monash 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 87.5 | 0 | 0.069 | 0.061 | 0.055 | 0.045 | 0.039 | 0.030 | 0.024 |
| 2000 | 57.9 | 0 | 0.054 | 0.047 | 0.044 | 0.041 | 0.032 | 0.027 | 0.022 |
| 2001 | 81.5 | 0 | 0.062 | 0.044 | 0.041 | 0.038 | 0.034 | 0.030 | 0.026 |
| 2002 | 93.5 | 0 | 0.063 | 0.055 | 0.052 | 0.047 | 0.042 | 0.032 | 0.024 |
| 2003 | 92.4 | 0 | 0.102 | 0.069 | 0.061 | 0.050 | 0.045 | 0.035 | 0.025 |
| 2004 | 94.1 | 0 | 0.064 | 0.56 | 0.054 | 0.048 | 0.044 | 0.038 | 0.030 |
| 2005 | 97.8 | 0 | 0.065 | 0.058 | 0.053 | 0.045 | 0.041 | 0.034 | 0.030 |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 20: Statistical summary for daily maximum 1-hour O3 Monash 1999 – 2009

Table 18: Statistical summary for daily maximum 1-hour O3 Civic 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 64.6 | 0 | 0.091 | 0.056 | 0.051 | 0.040 | 0.035 | 0.027 | 0.023 |
| 2000 | 51.9 | 0 | 0.053 | 0.048 | 0.045 | 0.038 | 0.035 | 0.028 | 0.018 |
| 2001 | 88.3 | 0 | 0.055 | 0.050 | 0.046 | 0.043 | 0.040 | 0.035 | 0.028 |
| 2002 | 79.8 | 0 | 0.082 | 0.060 | 0.053 | 0.049 | 0.044 | 0.035 | 0.029 |
| 2003 | 93.6 | 0 | 0.094 | 0.065 | 0.055 | 0.049 | 0.045 | 0.037 | 0.031 |
| 2004 | 93.5 | 0 | 0.071 | 0.055 | 0.053 | 0.045 | 0.041 | 0.034 | 0.028 |
| 2005 | 85.5 | 0 | 0.070 | 0.061 | 0.051 | 0.042 | 0.038 | 0.032 | 0.028 |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 21: Statistical summary for daily maximum 1-hour O3 Civic 1999 – 2009

Table 19: Statistical summary for daily maximum 4-hour O3 Monash 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 87.5 | 0 | 0.063 | 0.054 | 0.046 | 0.042 | 0.036 | 0.029 | 0.024 |
| 2000 | 57.9 | 0 | 0.047 | 0.043 | 0.041 | 0.035 | 0.030 | 0.026 | 0.019 |
| 2001 | 81.5 | 0 | 0.051 | 0.041 | 0.038 | 0.035 | 0.032 | 0.028 | 0.024 |
| 2002 | 93.5 | 0 | 0.058 | 0.051 | 0.049 | 0.044 | 0.039 | 0.031 | 0.023 |
| 2003 | 92.4 | 1 | 0.082 | 0.063 | 0.058 | 0.048 | 0.043 | 0.033 | 0.025 |
| 2004 | 94.1 | 0 | 0.060 | 0.053 | 0.051 | 0.045 | 0.042 | 0.036 | 0.029 |
| 2005 | 97.5 | 0 | 0.062 | 0.054 | 0.049 | 0.044 | 0.039 | 0.033 | 0.029 |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 22: Statistical summary for daily maximum 4-hour O3 Monash 1999 – 2009

Table 20: Statistical summary for daily maximum 4-hour O3 Civic 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 64.6 | 0 | 0.053 | 0.050 | 0.044 | 0.036 | 0.030 | 0.025 | 0.021 |
| 2000 | 51.9 | 0 | 0.050 | 0.043 | 0.038 | 0.034 | 0.031 | 0.024 | 0.017 |
| 2001 | 88.3 | 0 | 0.048 | 0.045 | 0.043 | 0.041 | 0.038 | 0.032 | 0.026 |
| 2002 | 79.8 | 0 | 0.073 | 0.057 | 0.051 | 0.046 | 0.042 | 0.033 | 0.027 |
| 2003 | 93.6 | 0 | 0.078 | 0.055 | 0.051 | 0.046 | 0.042 | 0.036 | 0.029 |
| 2004 | 93.5 | 0 | 0.062 | 0.052 | 0.048 | 0.043 | 0.039 | 0.32 | 0.026 |
| 2005 | 85.5 | 0 | 0.061 | 0.054 | 0.047 | 0.040 | 0.036 | 0.031 | 0.026 |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 23: Statistical summary for daily maximum 4-hour O3 Civic 1999 – 2009

PM10

Table 21: Statistical summary for daily maximum 24-hour PM10 Monash 1999 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 9.0 | 4 | 65.11 | 65.0 | 64.9 | 63.6 | 51.3 | 37.7 | 21.1 |
| 2000 | 15.3 | 1 | 56.4 | 52.6 | 49.4 | 47.6 | 42.4 | 23.1 | 14.5 |
| 2001 | 15.9 | 4 | 70.6 | 66.1 | 61.9 | 56.2 | 45.6 | 25.0 | 13.9 |
| 2002 | 75 | 0 | 108.4 | 56.6 | 48.5 | 42.4 | 37.7 | 25.3 | 16.2 |
| 2003 | 97.5 | 13 | 350.4 | 136.4 | 105.3 | 39.6 | 30.3 | 21.2 | 14.6 |
| 2004 | 99.7 | 3 | 52.0 | 48.2 | 46.0 | 33.8 | 28.5 | 20.7 | 14.7 |
| 2005 | 97.5 | 10 | 98.8 | 57.6 | 52.7 | 37.3 | 31.0 | 21.2 | 14.5 |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |

70

60

50

40

30

20

10

0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008	2009

Figure 24: Statistical summary for daily maximum 24-hour PM10 Monash 1999 – 2009

2009 data has not been included in Figure 24 as insufficient data in quarters 1 and 2 (zero and twenty five percent respectively) has biased the percentile data.

Table 22: Statistical summary for daily maximum 24-hour PM10 Civic 1999 – 2008

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1999 | 9 | 4 | 65.1 | 65.0 | 64.9 | 63.6 | 51.3 | 37.7 | 21.1 |
| 2000 | 16.7 | 0 | 39.3 | 35.9 | 33.2 | 31.4 | 29.4 | 23.8 | 15.7 |
| 2001 | 14.8 | 0 | 33..6 | 33.3 | 32.7 | 27.5 | 26.2 | 20.8 | 16.2 |
| 2002 | 15.6 | 3 | 67.4 | 67.1 | 66.3 | 42.7 | 25.4 | 18.7 | 15.3 |
| 2003 | 12.6 | 0 | 20.8 | 20.8 | 20.7 | 19.3 | 17.3 | 13.6 | 9.3 |
| 2004 | 16.7 | 0 | 33.2 | 32.4 | 32.0 | 28.1 | 22.5 | 17.9 | 14.4 |
| 2005 | 9.6 | 1 | 50.64 | 47.2 | 43.8 | 34.8 | 27.5 | 19.5 | 12.7 |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |

70.0

60.0

50.0

40.0

30.0

20.0

10.0

0.0

1999	2000	2001	2002	2003	2004	2005	2006	2007	2008

Figure 25: Statistical summary for daily maximum 24-hour PM10 Civic 1999 – 2008

PM2.5

Table 23: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2009

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.1 | 15 | 38.3 | 35.8 | 31.5 | 23.5 | 16.6 | 9.5 | 6.2 |
| 2005 | 73.6 | 14 | 38.6 | 31.4 | 29.3 | 25.0 | 20.7 | 9.0 | 4.9 |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |

30.0

25.0

20.0

15.0

10.0

5.0

0.0

2004	2005	2006	2007	2008	2009

Figure 26: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2009

10

9

7

6

5

4

3

2

1

0

2004	2005	2006	2007	2008	2009

Figure 27: Annual average 24-hour PM2.5 Monash 2004 – 2009

# Text boxes

1%

1%

2%

1%

3%

92%

Motor vehicles Gasesous/other fuel Aeroplanes

Domestic wood heaters Lawn mowing

Other

1%

1%

2%

1%

18%

77%

Motor vehicles Domestic wood heaters Lawn mowing Barbeques

Aeroplanes

Burning Off

Domestic wood heaters Motor Vehicles Barbeques

Burning off

Gas/other fuel Lawn mowing

| Region/ Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra | 95.8 | 94.3 | 90.4 | 95.3 | 94.0 | 0 | Met |
| Monash |  |  |  |  |  |  |  |
| Civic | 95.6 | 95.5 | 91.3 | 84.8 | 91.2 | 0 | Met |

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

part per million

NEPM standard

parts per million

part per million

NEPM standard

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

parts per million

| Region/ Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra Monash | 0 | 25 | 78 | 69 | 82 | 9 | Not Met |

NEPM standard

micrograms per cubic metre

| Region/ Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration (g/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra Monash | 24 | 47 | 76 | 90 | 64 | 6.2 | 2 |

NEPM advisory standard

micrograms per cubic metre

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 353 | 2.0 | 9 May 02:00 | 1.8 | 12 June 02:00 |
| Monash |  |  |  |  |  |
| Civic | 348 | 1.9 | 21 Jul 23:00 | 1.9 | 11 Aug 22:00 |

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 339 | 0.041 | 30 Jan 08:00 | 0.035 | 3 Dec 22:00 |
| Monash |  |  |  |  |  |
| Civic | 291 | 0.043 | 19 Nov 19:00 | 0.041 | 6 Feb 06:00 |

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 353 | 0.073 | 30 Jan 13:00 | 0.070 | 31 Jan 10:00 |
| Monash |  |  |  |  |  |
| Civic | 358 | 0.060 | 30 Jan 13:00 | 0.060 | 31 Jan 13:00 |

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 352 | 0.068 | 30 Jan 13:00 | 0.066 | 31 Jan 17:00 |
| Monash |  |  |  |  |  |
| Civic | 358 | 0.059 | 30 Jan 13:00 | 0.055 | 31 Jan 16:00 |

| Region/ Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Canberra Monash | 155 | 210 | 22 Sept | 53.3 | 29 Aug |

| Region/ Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Canberra Monash | 236 | 33.5 | 9 Aug | 19.7 | 11 Aug |

NEPM Standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

NEPM standard

parts per million

NEPM standard

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM advisory standard

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre