ACT AIR QUALITY REPORT 2015

# Environment Protection Authority | June 2016

# TABLE OF CONTENTS

TABLE OF CONTENTS	i

LIST OF TABLES	ii

LIST OF FIGURES	iii

LIST OF DEFINITIONS AND ABBREVIATIONS	iv

OVERVIEW	1

Current Performance Monitoring Stations	2

Monitoring Methods	3

NATA Accreditation Status	3

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND GOALS	4

Carbon monoxide	6

Nitrogen dioxide	7

Ozone	9

Particulate matter PM10	12

Particulate matter PM2.5	14

ANALYSIS OF AIR QUALITY MONITORING	16

Carbon monoxide	16

Nitrogen dioxide	16

Ozone	17

Particulate matter PM10	18

Particulate matter PM2.5	18

ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL	19

APPENDIX A: STATISTICAL SUMMARY AND TRENDS	20

Carbon monoxide	20

Nitrogen dioxide	21

Ozone	22

PM10	26

PM2.5	28

# LIST OF TABLES

Table 1 Summary of stations’ siting compliance with AS 3580.1.1:2007	2

Table 2 Methods used for monitoring AAQ NEPM pollutants	3

Table 3: AAQ NEPM standards and goals	4

Table 4: 2015 compliance summary for CO	6

Table 5: 2015 compliance summary for NO2	7

Table 6: 2015 compliance summary for O3	9

Table 7: 2015 compliance summary for PM10	12

Table 8: 2015 compliance summary for PM2.5	14

Table 9: 2015 summary statistics for daily peak 8-hour CO	16

Table 10: 2015 summary statistics for daily peak 1-hour NO2	16

Table 11: 2015 summary statistics for daily peak 1-hour O3	17

Table 12: 2015 summary statistics for daily peak 4-hour O3	17

Table 13: 2015 summary statistics for daily peak PM10	18

Table 14: 2015 summary statistics for daily peak PM2.5	18

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2006 – 2015	20

Table 16: Statistical summary for daily maximum 1-hour NO2 Monash 2006 – 2015	21

Table 17: Statistical summary for daily maximum 1-hour O3 Monash 2006 – 2015	22

Table 18: Statistical summary for daily maximum 1-hour O3 Civic 2006 – 2015	23

Table 19: Statistical summary for daily maximum 4-hour O3 Monash 2006 – 2015	24

Table 20: Statistical summary for daily maximum 4-hour O3 Civic 2006 – 2015	25

Table 21: Statistical summary for daily maximum 24-hour PM10 Monash 2006 – 2015	26

Table 22: Statistical summary for daily maximum 24-hour PM10 Civic 2006 – 2015	27

Table 23: Statistical summary for daily maximum 24-hour PM2.5 Monash 2006 – 2015	28

# LIST OF FIGURES

Figure 1: Daily max for CO 8-hour average – Monash	6

Figure 2: Daily max for CO 8-hour average – Florey	7

Figure 3: Daily max for NO2 – Monash	8

Figure 4: Daily max for NO2 – Florey	8

Figure 5: Daily max for 1 hour O3 – Monash	9

Figure 6: Daily max for 1 hour O3 – Civic	10

Figure 7: Daily max for 1 hour O3 – Florey	10

Figure 8: Daily max for 4 hours O3 - Monash	11

Figure 9: Daily max for 4 hours O3 – Civic	11

Figure 10: Daily max for 4 hours O3 – Florey	12

Figure 11: Daily max for PM10 – Monash	13

Figure 12: Daily max for PM10 – Civic	13

Figure 13: Daily max for PM10 – Florey	14

Figure 14: Daily max for PM2.5 – Monash	15

Figure 15: Daily max for PM2.5 – Florey	15

Figure 16: Statistical summary for daily maximum 8-hour CO Monash 2006 – 2015	20

Figure 17: Statistical summary for daily maximum 1-hour NO2 Monash 2006 – 2015	21

Figure 18: Annual average 1-hour NO2 Monash 2006 – 2015	22

Figure 19: Statistical summary for daily maximum 1-hour O3 Monash 2006 – 2015	23

Figure 20: Statistical summary for daily maximum 1-hour O3 Civic 2006 – 2015	24

Figure 21: Statistical summary for daily maximum 4-hour O3 Monash 2006 – 2015	25

Figure 22: Statistical summary for daily maximum 4-hour O3 Civic 2006 – 2015	26

Figure 23: Statistical summary for daily maximum 24-hour PM10 Monash 2006 – 2015	27

Figure 24: Statistical summary for daily maximum 24-hour PM10 Civic 2006 – 2015	28

Figure 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2006 – 2015	29

Figure 26: Annual average 24-hour PM2.5 Monash 2006 - 2015	29

# LIST OF DEFINITIONS AND ABBREVIATIONS

| Term | Definition |
| --- | --- |
| AAQ NEPM | National Environment Protection (Ambient Air Quality ) Measure |
| ACT | Australian Capital Territory |
| CO | Carbon Monoxide |
| BAM | Beta Attenuation Monitor |
| NATA | National Association of Testing Authorities |
| ND | Not Demonstrated |
| NO2 | Nitrogen Dioxide |
| O3 | Ozone |
| PMS | Performance Monitoring Station |
| PM2.5 | Particles with an equivalent aerodynamic diameter less than or equal to 2.5 Micrometers |
| PM10 | Particles with an equivalent aerodynamic diameter less than or equal to 10 Micrometers |
| ppm | Parts per million by volume – parts of pollutant per million parts of air |
| Q | Quarter (e.g. Q1 means the first quarter of the year) |
| SO2 | Sulfur Dioxide |
| µg/m3 | micrograms per cubic metre |

# OVERVIEW

##### Purpose

This report presents the results of ambient air quality monitoring in the ACT for the 2015 calendar year and assesses them in accordance with the requirements of the National Environment  Protection (Ambient Air Quality) Measure (AAQ NEPM) which was made by the National Environment Protection Council on 26 June 1998. A Variation to the AAQ NEPM was published on 15 December 2015. However, the varied AAQ NEPM wasn’t formally registered at the Federal Register of Legislation until March 2016. Therefore, air quality in 2015 has been assessed against the original AAQ NEPM standards and the associated goals shown in Table 3.

The AAQ NEPM establishes:

- requirements for monitoring air quality;

- air quality standards that are levels of specified pollutants against which air quality can be assessed; and

- a goal that the air quality standards be met to the extent specified in the NEPM. Recognising that certain events can impact on air quality, the NEPM specifies a maximum number of days on which it is permissible to exceed the standard.

##### ACT monitoring

The ACT monitors four of the six NEPM pollutants:

- carbon monoxide (CO);

- nitrogen dioxide (NO2);

- photochemical oxidants as ozone (O3); and

- particulate matter (particles less than 10 microns in diameter – PM10 and particles less than

2.5 microns in diameter – PM2.5).

Due to a lack of heavy industry, the ACT has never monitored sulfur dioxide (SO2) as it is primarily an industrial pollutant, and lead monitoring ceased in 2002 with the phase out of leaded petrol.

Monitoring was performed in accordance with the ACT’s monitoring plan, AAQ NEPM Technical Papers and ACT Health’s accreditation by the National Association of Testing Authorities (NATA).

##### Outcomes

Monitoring results demonstrate that Canberra’s air quality in 2015 was excellent, with no exceedences of the AAQ NEPM standards for carbon monoxide, nitrogen dioxide and photochemical oxidants as ozone. The major impacts on Canberra’s air quality in 2015 came from the accumulation of combustion particles from wood heaters. Once during 2015, air quality was also impacted by a dust storm in the region. The long-term trends show the ACT is meeting the goals of the NEPM.

MONITORING SUMMARY

Current Performance Monitoring Stations

The ACT Government has been conducting ambient air quality monitoring in Canberra since the early 1990’s. The Health Directorate is responsible for the Government’s ambient air quality        monitoring network. The Environment Protection Authority within the Chief Minister’s, Treasury and Economic Development Directorate is responsible for annual reporting under the AAQ NEPM.

The AAQ NEPM monitoring network in the ACT consists of three monitoring stations: at Monash, Civic and Florey. The Monash station is about 300 metres west of Cockcroft Avenue in the Monash district playing fields. The Civic station is located at the northern end of the carpark on the western side of the Olympic swimming pool adjacent to Allara Street. The Florey station is located at the end of Neumann Place, Florey on public land. The compliance and non-compliance criteria for the above stations against the siting standard AS/NZS 3580.1.1:2007 are listed in Table 1 below.

##### Table 1 Summary of stations’ siting compliance with AS 3580.1.1:2007

| Station | Height above ground | Minimum distance to support structure | Clear sky angle of 120° | Unrestricted airflow of 270°/360° | 20m from trees | No boilers or incinerators nearby | Minimum distance from road or traffic |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Monash |  |  |  |  |  |  |  |
| Civic |  |  |  |  |  |  |  |
| Florey |  |  |  |  |  |  |  |

Both Monash and Florey stations contain instrumentation that continuously monitors carbon monoxide, nitrogen dioxide, photochemical oxidants as ozone and both types of particle matters. The Civic station only monitors photochemical oxidants as ozone and particulate matter PM10.

### Monitoring Methods

The ACT monitoring is conducted in accordance with the relevant Australian standards as shown in Table 2. Data not meeting the requirements of these Standards are identified as invalid and not included in this report.

##### Table 2 Methods used for monitoring AAQ NEPM pollutants

| Pollutant | Standard | Title | Method Used |
| --- | --- | --- | --- |
| Carbon Monoxide | AS 3580.7.1-2011 | Ambient Air – Determination of Carbon Monoxide – Direct Reading Instrument Method | Gas filter correlation/ Infrared. |
| Nitrogen dioxide | AS 3580.5.1-2011 | Ambient Air – Determination of Oxides of Nitrogen – Chemiluminescence Method | Gas phase chemiluminescence. |
| Photochemical oxidant (ozone) | AS 3580.6.1-2011 | Ambient Air – Determination of Ozone – Direct Reading Instrument Method | Non-dispersive ultraviolet. |
| Particles PM10 | AS 3580.9.11-2008 | Method for sampling and analysis of ambient air Method – Determination of suspended particles matter – PM10 beta attenuation monitors | Beta Attenuation Monitor (BAM) |
| PM10 | AS/NZS 3580.9.6- 2005 | Methods for sampling and analysis of ambient air - Determination of suspended particulate matter - PM10 high volume sampler with size- selective inlet - Gravimetric method | Gravimetric reference method |
| PM2.5 | AS/NZS 3580.9.10- 2006 | Reference Method for the Determination of Fine Particulate matter as PM2.5 in the Atmosphere | Gravimetric reference Method |

NATA Accreditation Status

The ACT Government monitoring network is accredited by NATA for the measurement of all AAQ NEPM pollutants except sulfur dioxide as required under Clause 12 of the AAQ NEPM.

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND GOALS

For the purpose of this report, air quality is assessed against the AAQ NEPM standards and goals as specified in Schedule 2 of the AAQ NEPM and reproduced in Table 3.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3, Table 3).

The goal of the AAQ NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specified in Schedule 2 of the AAQ NEPM. The extent is expressed as a maximum allowable number of exceedences for each standard (shown in column 4, Table 3). These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfires, which cannot be controlled through normal air quality management programs.

The AAQ NEPM also specifies advisory reporting standards for PM2.5. The goal for PM2.5 is to collect sufficient data to facilitate a review of the PM2.5 standards, which has been completed through the variation of the AAQ NEPM.

##### Table 3: AAQ NEPM standards and goals

| Pollutant | Averaging Period | Maximum concentration | Goal within 10 years Maximum allowable exceedences | Monitoring Station |
| --- | --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year | Monash Florey |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year None | Monash Florey |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year | Monash Florey Civic |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year None | Not monitored |
| Lead | 1 year | 0.050 μg/m3 | None | Not monitored |
| Particles as PM10 | 1 day | 50 μg/m3 | 5 days a year | Monash Florey Civic |
| Particles as PM2.5 | 1 day 1 year | 25 μg/m3 8 μg/m3 | Not applicable Not applicable | Monash Florey |

The following tables (Table 4 to Table 8) summarise compliance with the standards and goals of the AAQ NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded, the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

Air quality is assessed as complying with the AAQ NEPM (i.e. ’MET’) if the number of exceedences is no more than the number specified in Schedule 2 of the AAQ NEPM and data availability was at least 75% in each quarter of the year.

Air quality is assessed as not complying with the AAQ NEPM (i.e. ‘NOT MET’) if there is more than the number of exceedences specified in Schedule 2 of the AAQ NEPM.

Air quality is assessed as ‘NOT DEMONSTRATED’ (ND) if there has been insufficient data collected to demonstrate that the standards and goal have been met or not met.

These categories (i.e. MET, NOT MET and ND) are used in the tables on the following pages.

Carbon monoxide

During 2015, no exceedences of the carbon monoxide standard were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated.

##### Table 4: 2015 compliance summary for CO

AAQ NEPM standard - 9.0 ppm (8-hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 95.4 | 92.6 | 95.5 | 95.8 | 94.8 | 0 | MET |
| Florey | 95.5 | 93.8 | 94.3 | 95.8 | 94.9 | 0 | MET |

Monash

##### Figure 1: Daily max for CO 8-hour average – Monash

Florey

##### Figure 2: Daily max for CO 8-hour average – Florey

Nitrogen dioxide

During 2015, no exceedences of the nitrogen dioxide standards were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated.

##### Table 5: 2015 compliance summary for NO2

AAQ NEPM standard – 0.12 ppm (1-hour average), 0.03 ppm (1-year average)

##### er of our ences ys)

Performance against the standards and goal

Monash

##### Figure 3: Daily max for NO2 – Monash

Florey

##### Figure 4: Daily max for NO2 – Florey

Ozone

During 2015, no exceedences of the 1-hour and 4-hour standards for ozone were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated.

##### Table 6: 2015 compliance summary for O3

AAQ NEPM standard – 0.10 ppm (1-hour average), 0.08 ppm (4-hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Monash | 83.9 | 95.8 | 95.6 | 95.8 | 92.8 | 0 | 0 | MET | MET |
| Civic | 88.8 | 76.4 | 94.7 | 95.7 | 89.0 | 0 | 0 | MET | MET |
| Florey | 95.6 | 91.1 | 94.3 | 95.8 | 94.2 | 0 | 0 | MET | MET |

Monash

##### Figure 5: Daily max for 1 hour O3 – Monash

Civic

##### Figure 6: Daily max for 1 hour O3 – Civic

#### Florey

##### Figure 7: Daily max for 1 hour O3 – Florey

Monash

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0.00

##### Figure 8: Daily max for 4 hours O3 - Monash

Civic

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

##### Figure 9: Daily max for 4 hours O3 – Civic

Florey

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

##### Figure 10: Daily max for 4 hours O3 – Florey

Particulate matter PM10

During 2015, two exceedences of the 24-hour PM10 standard were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated.

##### Table 7: 2015 compliance summary for PM10

AAQ NEPM standard 50 g/m3 1-day average

| Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 100 | 94.5 | 98.4 | 100 | 98.4 | 0 | MET |
| Civic | 95.6 | 97.8 | 96.8 | 99.2 | 97.5 | 1 | MET |
| Florey | 91.1 | 95.6 | 96.8 | 98.4 | 95.6 | 1 | MET |

Monash

##### Figure 11: Daily max for PM10 – Monash

Civic

##### Figure 12: Daily max for PM10 – Civic

#### Florey

##### Figure 13: Daily max for PM10 – Florey

Particulate matter PM2.5

Six exceedences of the 24-hour advisory reporting standard were recorded, all at Monash, in 2015.

##### Table 8: 2015 compliance summary for PM2.5

AAQ NEPM standard – 25 g/m3 (1-day), 8 g/m3 (1-year)

| Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration (g/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 95.6 | 97.8 | 91.9 | 98.4 | 96.4 | 7.4 | 6 |
| Florey | 98.9 | 98.9 | 100 | 90.2 | 96.2 | 6.5 | 0 |

Monash

##### Figure 14: Daily max for PM2.5 – Monash

30.0

#### Florey

25.0

20.0

15.0

10.0

5.0

0.0

##### Figure 15: Daily max for PM2.5 – Florey

ANALYSIS OF AIR QUALITY MONITORING

Annual summary statistics contained in Table 9 to Table 14 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The AAQ NEPM states that the short-term standards should not be exceeded on more than one day for carbon monoxide, nitrogen dioxide and ozone, and on no more than five days per year for particulate matter PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

### Carbon monoxide

Carbon monoxide levels are well below the AAQ NEPM standard. The highest recorded value in the ACT during 2015 was 2.0ppm at Florey, which is 22% of the standard.

##### Table 9: 2015 summary statistics for daily peak 8-hour CO

AAQ NEPM standard - 9.0 ppm (8-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 365 365 | 1.9 2.0 | 25 May 05:00 25 Jun 04:00 | 1.8 1.8 | 14 Jun 04:00 30 Jun 04:00 |

### Nitrogen dioxide

Nitrogen dioxide levels are well below the AAQ NEPM standard. The highest recorded 1-hour value during 2015 was 0.033ppm at Florey, which is 27.5% of the standard.  The highest recorded annual average in 2015 was 0.005ppm at Florey (refer to table 5). This is 17% of the annual standard 0.03ppm.

##### Table 10: 2015 summary statistics for daily peak 1-hour NO2

AAQ NEPM standard 0.12 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 365 365 | 0.032 0.033 | 20 Apr 20:00 19 Aug 23:00 | 0.030 0.033 | 06 Oct 21:00 15 Oct 20:00 |

### Ozone

Ozone levels are below the AAQ NEPM standard. The highest recorded 1-hour value in the ACT during 2015 was 0.065ppm at Monash, which is 87% of the standard. The highest recorded 4-hour value in the ACT during 2015 was 0.050ppm at Monash, which is 62.5% of the standard.

##### Table 11: 2015 summary statistics for daily peak 1-hour O3

AAQ NEPM standard 0.10 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 365 365 365 | 0.065 0.042 0.040 | 13 Feb 11:00 03 Jan 12:00 17 Dec 17:00 | 0.052 0.042 0.039 | 28 Feb 17:00 07 Jan 14:00 20 Nov 18:00 |

##### Table 12: 2015 summary statistics for daily peak 4-hour O3

AAQ NEPM standard 0.08 ppm (4-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 365 365 365 | 0.050 0.041 0.037 | 28 Feb 18:00 03 Jan 15:00 17 Dec 17:00 | 0.049 0.041 0.037 | 17 Dec 17:00 02 Jan 16:00 06 Oct 17:00 |

### Particulate matter PM10

During 2015, the PM10 standard was exceeded once at Civic and Florey respectively due to a dust storm. The highest PM10 level recorded during 2015 was 70.8μg/m3 at Florey on 05 May 2015.

##### Table 13: 2015 summary statistics for daily peak PM10

AAQ NEPM standard 50 g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 359 356 349 | 49.4 64.3 70.8 | 05 May 05 May 05 May | 24.5 26.9 26.1 | 06 June 20 November 20 November |

### Particulate matter PM2.5

The 24-hour advisory reporting standard for PM2.5 was exceeded six times at Monash. These exceedences occurred during late May and July due to domestic wood heater emissions.

##### Table 14: 2015 summary statistics for daily peak PM2.5

AAQ NEPM standard 25 g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 352 351 | 33.8 24.3 | 05 July 05 July | 26.4 20.2 | 24 May 14 June |

## ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL

The goals and standards have been consistently met in the ACT for carbon monoxide, nitrogen dioxide and ozone since the commencement of the AAQ NEPM.

Historical monitoring results indicate that the only AAQ NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions from domestic wood heaters.  In more recent years exceedences of the particulate matter standards have also been attributed to dust storms and smoke from controlled burns.

The ACT Government for many years has actively worked on addressing the causes for the exceedences attributable to domestic wood heaters. For example, the ACT Government has introduced the licensing of firewood merchants, has a wood heater replacement program and has run a range of public awareness campaigns, such as the ‘Burn Right Tonight’ campaign. It will continue to implement an integrated program to address woodsmoke.

The following section provides a basic statistical summary, using percentiles, for Monash and Civic stations and for each standard. Percentiles for daily maximum values are presented. As the Florey station was established in 2014, there is insufficient data to show the statistical summary and trends.

Carbon monoxide

##### Table 15: Statistical summary for daily maximum 8-hour CO Monash 2006 – 2015

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2010 | 99.2 | 0 | 1.8 | 1.7 | 1.6 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2011 | 98.6 | 0 | 2.2 | 1.9 | 1.8 | 1.5 | 1.1 | 0.5 | 0.2 |
| 2012 | 99.7 | 0 | 1.8 | 1.7 | 1.7 | 1.2 | 1.0 | 0.6 | 0.3 |
| 2013 | 95.9 | 0 | 2.1 | 1.9 | 1.8 | 1.5 | 1.2 | 0.6 | 0.3 |
| 2014 | 94.0 | 0 | 1.8 | 1.6 | 1.5 | 1.4 | 1.1 | 0.7 | 0.4 |
| 2015 | 94.8 | 0 | 1.9 | 1.7 | 1.6 | 1.4 | 1.1 | 0.6 | 0.3 |

10.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

### Nitrogen dioxide

##### Table 16: Statistical summary for daily maximum 1-hour NO2 Monash 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |
| 2010 | 89.1 | 0 | 0.037 | 0.029 | 0.028 | 0.025 | 0.023 | 0.021 | 0.017 |
| 2011 | 96.7 | 0 | 0.043 | 0.031 | 0.030 | 0.029 | 0.026 | 0.022 | 0.015 |
| 2012 | 97.5 | 0 | 0.033 | 0.030 | 0.029 | 0.026 | 0.025 | 0.021 | 0.014 |
| 2013 | 97.5 | 0 | 0.037 | 0.031 | 0.030 | 0.027 | 0.025 | 0.021 | 0.014 |
| 2014 | 94.1 | 0 | 0.036 | 0.030 | 0.029 | 0.027 | 0.025 | 0.020 | 0.015 |
| 2015 | 94.8 | 0 | 0.032 | 0.028 | 0.027 | 0.026 | 0.024 | 0.020 | 0.014 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 17: Statistical summary for daily maximum 1-hour NO2 Monash 2006 – 2015

0.025

0.020

0.015

0.010

0.005

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 18: Annual average 1-hour NO2 Monash 2006 – 2015

Ozone

Table 17: Statistical summary for daily maximum 1-hour O3 Monash 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |
| 2010 | 86.6 | 0 | 0.051 | 0.048 | 0.046 | 0.042 | 0.037 | 0.033 | 0.030 |
| 2011 | 99.2 | 0 | 0.056 | 0.052 | 0.047 | 0.044 | 0.040 | 0.033 | 0.028 |
| 2012 | 100 | 0 | 0.055 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.062 | 0.051 | 0.049 | 0.045 | 0.041 | 0.035 | 0.029 |
| 2014 | 94.8 | 0 | 0.087 | 0.060 | 0.057 | 0.050 | 0.044 | 0.036 | 0.030 |
| 2015 | 92.8 | 0 | 0.065 | 0.050 | 0.046 | 0.044 | 0.040 | 0.034 | 0.026 |

0.100

0.080

0.060

0.040

0.020

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 19: Statistical summary for daily maximum 1-hour O3 Monash 2006 – 2015

Table 18: Statistical summary for daily maximum 1-hour O3 Civic 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |
| 2010 | 99.2 | 0 | 0.058 | 0.050 | 0.048 | 0.040 | 0.036 | 0.029 | 0.025 |
| 2011 | 96.4 | 0 | 0.052 | 0.046 | 0.045 | 0.041 | 0.036 | 0.030 | 0.026 |
| 2012 | 100 | 0 | 0.053 | 0.041 | 0.038 | 0.034 | 0.030 | 0.024 | 0.020 |
| 2013 | 92.1 | 0 | 0.060 | 0.043 | 0.041 | 0.036 | 0.032 | 0.028 | 0.024 |
| 2014 | 94.0 | 0 | 0.060 | 0.050 | 0.046 | 0.039 | 0.036 | 0.028 | 0.022 |
| 2015 | 89.0 | 0 | 0.042 | 0.039 | 0.037 | 0.034 | 0.031 | 0.026 | 0.022 |

0.080

0.060

0.040

0.020

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 20: Statistical summary for daily maximum 1-hour O3 Civic 2006 – 2015

Table 19: Statistical summary for daily maximum 4-hour O3 Monash 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |
| 2010 | 86.6 | 0 | 0.049 | 0.046 | 0.043 | 0.040 | 0.037 | 0.032 | 0.029 |
| 2011 | 98.9 | 0 | 0.054 | 0.048 | 0.044 | 0.041 | 0.038 | 0.032 | 0.027 |
| 2012 | 99.7 | 0 | 0.052 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.059 | 0.048 | 0.047 | 0.042 | 0.039 | 0.033 | 0.028 |
| 2014 | 94.8 | 0 | 0.060 | 0.055 | 0.052 | 0.046 | 0.042 | 0.034 | 0.029 |
| 2015 | 92.8 | 0 | 0.050 | 0.046 | 0.044 | 0.041 | 0.039 | 0.033 | 0.025 |

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 21: Statistical summary for daily maximum 4-hour O3 Monash 2006 – 2015

Table 20: Statistical summary for daily maximum 4-hour O3 Civic 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |
| 2010 | 99.2 | 0 | 0.056 | 0.047 | 0.044 | 0.037 | 0.034 | 0.028 | 0.024 |
| 2011 | 96.4 | 0 | 0.050 | 0.044 | 0.041 | 0.038 | 0.035 | 0.029 | 0.025 |
| 2012 | 100 | 0 | 0.042 | 0.037 | 0.036 | 0.032 | 0.028 | 0.023 | 0.019 |
| 2013 | 91.8 | 0 | 0.057 | 0.040 | 0.038 | 0.034 | 0.030 | 0.027 | 0.023 |
| 2014 | 94.0 | 0 | 0.047 | 0.045 | 0.040 | 0.036 | 0.034 | 0.026 | 0.020 |
| 2015 | 89.0 | 0 | 0.041 | 0.038 | 0.035 | 0.031 | 0.029 | 0.025 | 0.021 |

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 22: Statistical summary for daily maximum 4-hour O3 Civic 2006 – 2015

PM10

##### Table 21: Statistical summary for daily maximum 24-hour PM10 Monash 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |
| 2010 | 95.4 | 0 | 48.4 | 35.6 | 27.4 | 23.5 | 20.2 | 14.7 | 10.0 |
| 2011 | 99.2 | 0 | 40.0 | 33.7 | 30.3 | 22.8 | 18.6 | 13.2 | 8.7 |
| 2012 | 98.6 | 0 | 41.0 | 24.2 | 21.8 | 19.7 | 17.4 | 13.7 | 9.7 |
| 2013 | 95.6 | 0 | 43.5 | 29.1 | 25.1 | 20.2 | 16.8 | 13.1 | 8.9 |
| 2014 | 97.8 | 0 | 39.3 | 27.1 | 23.1 | 19.1 | 16.4 | 12.9 | 9.6 |
| 2015 | 98.4 | 0 | 49.4 | 25.3 | 23.3 | 19.5 | 17.3 | 13.1 | 9.5 |

50.0

40.0

30.0

20.0

10.0

0.0

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 23: Statistical summary for daily maximum 24-hour PM10 Monash 2006 – 2015

Note: 2009 data has not been included in Figure 23 as the percentile data has been skewed because of insufficient data in Q1 and Q2 (zero and twenty five percent respectively) and the extreme readings associated with the dust storm which affected most of eastern Australia on 22 and 23 September, 2009.

##### Table 22: Statistical summary for daily maximum 24-hour PM10 Civic 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |
| 2009 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 2010 | 57.6 | 0 | 23.8 | 19.7 | 17.1 | 14.7 | 13.7 | 11.1 | 8.4 |
| 2011 | 97.0 | 0 | 29.2 | 22.3 | 20.9 | 16.9 | 14.4 | 11.0 | 7.9 |
| 2012 | 95.1 | 0 | 49.5 | 22.8 | 20.2 | 17.0 | 14.9 | 12.1 | 8.7 |
| 2013 | 92.9 | 1 | 57.8 | 26.5 | 24.4 | 19.9 | 15.8 | 12.0 | 8.6 |
| 2014 | 95.1 | 0 | 31.4 | 24.2 | 22.1 | 17.7 | 15.1 | 12.6 | 9.3 |
| 2015 | 97.5 | 1 | 64.3 | 27.9 | 25.0 | 20.9 | 17.6 | 14.1 | 10.4 |

50.0

40.0

30.0

20.0

10.0

0.0

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

Figure 24: Statistical summary for daily maximum 24-hour PM10 Civic 2006 – 2015 Note: No PM10 monitoring was conducted at Civic in 2009.

PM2.5

##### Table 23: Statistical summary for daily maximum 24-hour PM2.5 Monash 2006 – 2015

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |
| 2010 | 95.1 | 2 | 52.4 | 22.1 | 20.9 | 17.4 | 14.3 | 7.8 | 4.4 |
| 2011 | 92.1 | 4 | 32.8 | 25.6 | 22.9 | 20.0 | 12.5 | 7.0 | 4.5 |
| 2012 | 95.1 | 3 | 29.2 | 23.8 | 19.8 | 16.5 | 13.2 | 8.3 | 5.0 |
| 2013 | 98.6 | 6 | 38.4 | 30.5 | 22.7 | 19.2 | 12.9 | 8.1 | 5.2 |
| 2014 | 87.7 | 4 | 31.5 | 25.7 | 21.6 | 18.7 | 14.4 | 8.6 | 5.6 |
| 2015 | 96.4 | 6 | 33.8 | 26.9 | 23.3 | 19.0 | 14.6 | 8.2 | 5.6 |

30.0

25.0

20.0

15.0

10.0

5.0

0.0

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2006 – 2015

10.0

9.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2006	2007	2008	2009	2010	2011	2012	2013	2014	2015

##### Figure 26: Annual average 24-hour PM2.5 Monash 2006 - 2015

# Text boxes

NEPM standard

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

parts per million

NEPM standard

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

parts per million

| Performance monitoring station | Numb Data availability rates Annual mean 1 h (% of hours) Concentration exceed (ppm) (da |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | 1 hour | 1 year |
|  | Q1 | Q2 Q3 Q4 Annual |  |  |  |  |  |  |
| Monash Florey | 95.4 95.5 | 95.4 92.7 95.8 94.8 86.3 88.4 95.8 91.5 | 0.0 | 04 0 0.005 0 |  |  | MET MET | MET MET |

parts per million

NEPM standard

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

parts per million

NEPM standard

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

parts per million

NEPM standard

0.120

0.100

0.080

0.060

0.040

0.020

0.000

parts per million

NEPM standard

0.120

0.100

0.080

0.060

0.040

0.020

0.000

parts per million

NEPM standard

0.120

0.100

0.080

0.060

0.040

0.020

0.000

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

parts per million

micrograms per cubic metre

NEPM standard

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

NEPM standard

70.0

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

NEPM standard

80.0

70.0

60.0

50.0

40.0

30.0

20.0

10.0

0.0

NEPM advisory standard

40.0

35.0

30.0

25.0

20.0

15.0

10.0

5.0

0.0

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre

NEPM Standard

95 %ile

75 %ile

50 %ile

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

parts per million

NEPM standard

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

micrograms per cubic metre

NEPM standard

95 %ile 75 %ile 50 %ile

NEPM Standard

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM advisory standard

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre