ACT AIR QUALITY REPORT 2010

Environment Protection Authority | June 2011

# TABLE OF CONTENTS

LIST OF TABLES	ii

LIST OF FIGURES	iii

LIST OF DEFINITIONS AND ABBREVIATIONS	iv

OVERVIEW	1

MONITORING SUMMARY	2

Current Performance Monitoring Stations	2

Monitoring Methods	2

NATA Accreditation Status	3

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL	4

Carbon monoxide	5

Nitrogen dioxide	6

Ozone	8

PM10	10

PM2.5	12

ANALYSIS OF AIR QUALITY MONITORING	13

Carbon monoxide	13

Nitrogen dioxide	13

Ozone	14

PM10	14

PM2.5	15

The 24-hour advisory reporting standard for PM2.5 was exceeded at Monash on 19 and 20 March 2010 (52.4 μg/m3 and 27.5 μg/m3 respectively) because of a number of large hazard reduction burns in NSW	15

ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL	16

APPENDIX A: STATISTICAL SUMMARY AND TRENDS	17

Carbon monoxide	17

Nitrogen dioxide	19

Ozone	22

PM10	26

PM2.5	28

# LIST OF TABLES

Table 1 Summary of stations’ siting compliance with AS 3580.1.1-2007	2

Table 2 Methods used for monitoring AAQ NEPM pollutants	3

Table 3: NEPM standards and goals	4

Table 4: 2010 compliance summary for CO	5

Table 5: 2010 compliance summary for NO2	6

Table 6: 2010 compliance summary for O3	8

Table 7: 2010 compliance summary for PM10	10

Table 8: 2010 compliance summary for PM2.5	12

Table 9: 2010 summary statistics for daily peak 8-hour CO	13

Table 10: 2010 summary statistics for daily peak 1-hour NO2	13

Table 11: 2010 summary statistics for daily peak 1-hour O3	14

Table 12: 2010 summary statistics for daily peak 4-hour O3	14

Table 13: 2010 summary statistics for daily peak PM10	14

Table 14: 2010 summary statistics for daily peak PM2.5	15

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2001 – 2010	17

Table 16: Statistical summary for daily maximum 8-hour CO Civic 2001 – 2010	18

Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2001 – 2010	19

Table 18: Statistical summary for daily maximum 1-hour NO2 Civic 2001 – 2010	20

Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2001 – 2010	22

Table 20: Statistical summary for daily maximum 1-hour O3 Civic 2001 – 2010	23

Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2001 – 2010	24

Table 22: Statistical summary for daily maximum 4-hour O3 Civic 2001 – 2010	25

Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2001 – 2010	26

Table 24: Statistical summary for daily maximum 24-hour PM10 Civic 2001 – 2010	27

Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2010	28

# LIST OF FIGURES

Figure 1: Daily max for CO 8-hr average - Monash	5

Figure 2: Daily max for CO 8-hr average - Civic	6

Figure 3: Daily max for NO2 - Monash	7

Figure 4: Daily max for NO2 – Civic	7

Figure 5: Daily max for 1 hour O3 – Monash	8

Figure 6: Daily max for 1 hour O3 – Civic	9

Figure 7: Daily max for 4 hours O3 - Monash	9

Figure 8: Daily max for 4 hours O3 - Civic	10

Figure 9: Daily max for PM10 – Monash.	11

Figure 10: Daily max for PM10 – Civic.	11

Figure 11: Daily max for PM2.5 – Monash.	12

Figure 12: Statistical summary for daily maximum 8-hour CO Monash 2001 – 2010	17

Figure 13:  Statistical summary for daily maximum 8-hour CO Civic 2001 – 2010	18

Figure 14: Statistical summary for daily maximum 1-hour NO2 Monash 2001 – 2010	19

Figure 15: Statistical summary for daily maximum 1-hour NO2 Civic 2001 – 2010	20

Figure 16: Annual average 1-hour NO2 Monash 2001 – 2010	21

Figure 17: Annual average 1-hour NO2 Civic 2001 – 2010	21

Figure 18: Statistical summary for daily maximum 1-hour O3 Monash 2001 – 2010	22

Figure 19: Statistical summary for daily maximum 1-hour O3 Civic 2001 – 2010	23

Figure 20: Statistical summary for daily maximum 4-hour O3 Monash 2001 – 2010	24

Figure 21: Statistical summary for daily maximum 4-hour O3 Civic 2001 – 2010	25

Figure 22: Statistical summary for daily maximum 24-hour PM10 Monash 2001 – 2010	26

Figure 23: Statistical summary for daily maximum 24-hour PM10 Civic 2001 – 2008	27

Figure 24: Statistical summary for daily maixum 24-hour PM2.5 Monash 2004 – 2010	28

Figure 25: Annual average 24-hour PM2.5 Monash 2004 - 2010	29

# LIST OF DEFINITIONS AND ABBREVIATIONS

AAQ NEPM	National Environment Protection (Ambient Air Quality ) Measure ACT	Australian Capital Territory

CO	Carbon Monoxide

BAM	Beta Attenuation Monitor

EPHC	Environment Protection and Heritage Council

ESDD	Environment and Sustainable Development Directorate NATA	National Association of Testing Authorities

ND	Not Demonstrated

NEPC	National Environment Protection Council NO2	Nitrogen Dioxide

NPI	National Pollutant Inventory

O3	Ozone

NSW	New South Wales

PMS	Performance Monitoring Station

PM2.5	Particles with an equivalent aerodynamic diameter less than or equal to 2.5 micrometers

PM10	Particles with an equivalent aerodynamic diameter less than or equal to 10 micrometers

ppm	Parts per million by volume – parts of pollutant per million parts of air PRC	Peer Review Committee

SO2	Sulphur Dioxide

µg/m3	micrograms per cubic metre

# OVERVIEW

This report presents the results of air quality monitoring in the ACT for the 2010 calendar year and assesses them in accordance with the requirements of the National Environment Protection (Ambient Air Quality) Measure (AAQ NEPM) which was made by the National Environment Protection Council on 26 June 1998.

Canberra’s overall air quality compared to other capital cities is excellent.  However it does experience elevated particle pollution during winter because of emissions from domestic wood heaters. The ACT Government acknowledges the problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

Monitoring results demonstrate that the major impacts on Canberra’s air quality in 2010, as in previous years, came from the accumulation of combustion particles from wood heaters in cold, highly stable air, hazard reduction burns and dust storms. With the exception of particulate matter less than 2.5 microns (PM2.5) all measured parameters are below the AAQ NEPM standards.

There were two exceedances of the PM2.5 24-hr advisory reporting standard which occurred on 19 and 20 March 2010.  These exceedences were because of smoke from a number of large hazard reduction burns in NSW. No exceedences of the advisory standard occurred during the winter months as a result of wood heater emissions.

Monitoring was performed in accordance with the ACT’s monitoring plan, AAQ NEPM Technical Papers and ACT Health’s NATA accreditation.

# MONITORING SUMMARY

## Current Performance Monitoring Stations

The ACT Government has been undertaking ambient air quality monitoring in Canberra since the early 1990’s. ACT Health is responsible for the Government’s ambient air quality monitoring network, which currently consists of two performance monitoring stations (PMS). The Environment and Sustainable Development Directorate (ESDD) is responsible for reporting compliance with the AAQ NEPM annually.

The ACT’s population has passed the threshold where it needs a second AAQ NEPM PMS, ACT Health has been working on establishing the second station. Until a second AAQ NEPM PMS can be established data from the Civic PMS, though not ideally located, will be used for annual report purposes.

The Monash PMS, which complies with the siting standard AS/NZS 3580.1.1:2007, is approximately 300 metres west of Cockcroft Avenue in the Monash district playing fields. The Civic PMS is located at the northern end of the carpark on the western side of the Olympic swimming pool adjacent to Allara Street. The compliance and non-compliance criteria for both PMS are listed in Table 1 below.

Table 1 Summary of stations’ siting compliance with AS 3580.1.1-2007

| Station | Location category | Height above ground | Minimum distance to support structure | Clear sky angle of 120° | Unrestricted airflow of 270°/360° | 20m from trees | No boilers or incinerators nearby | Minimum distance from road or traffic |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Monash | Residen tial |  |  |  |  |  |  |  |
| Civic | CBD |  |  |  |  |  |  |  |

Consistent with the ACT’s Ambient Air Quality Monitoring Plan, which was approved by the National Environment Protection Council (NEPC) in 2001, this report only covers four of  the six criteria pollutants, namely carbon monoxide (CO), nitrogen dioxide (NO2), photochemical oxidants as ozone (O3) and particulate matter less than 10 micrometres (PM10). Because of a lack of heavy industry the ACT has never monitored sulphur dioxide (SO2), and ceased monitoring lead in July 2002, following the phase out of leaded fuel on  1 January 2002, with ambient air lead levels being less than 2% of the standard. The report also covers particulate matter less than 2.5 micrometres (PM2.5).

Both stations contain instrumentation that continuously monitors CO, O3, and NO2. PM10 and PM2.5 monitoring is undertaken at Monash and PM10 monitoring resumed at Civic on 26 May 2010 following the installation of a new instrument.

## Monitoring Methods

The ACT monitoring is conducted in accordance with the relevant Australian standard as shown in Table 2.

Table 2 Methods used for monitoring AAQ NEPM pollutants

| Pollutant | Standard | Title | Method Used |
| --- | --- | --- | --- |
| Carbon Monoxide | AS 3580.7.1-1992 | Ambient Air – Determination of Carbon Monoxide – Direct Reading Instrument Method | Gas filter correlation/ Infrared. |
| Nitrogen dioxide | AS 3580.5.1-1993 | Ambient Air – Determination of Oxides of Nitrogen – Chemiluminescence Method | Gas phase chemiluminescence. |
| Photochemical oxidant (ozone) | AS 3580.6.1-1990 | Ambient Air – Determination of Ozone – Direct Reading Instrument Method | Non-dispersive ultraviolet. |
| Particles | AS 3580.9.11- | Method for sampling and | Beta Attenuation |
| PM10 | 2008 | analysis of ambient air | Monitor (BAM) |
|  |  | Method 9.11: |  |
|  |  | Determination of |  |
|  |  | suspended particles |  |
|  |  | matter – PM10 beta |  |
|  |  | attenuation monitors |  |
| PM10 | AS/NZS 3580.9.6- 2003 | Methods for sampling and analysis of ambient air - Determination of suspended particulate matter - PM10 high volume sampler with size- selective inlet - Gravimetric method | Gravimetric reference method |
| PM2.5 | AS/NZS 3580.9.10-2006 | Reference Method for the Determination of Fine Particulate matter as PM2.5 in the Atmosphere | Gravimetric reference method |

## NATA Accreditation Status

The ACT Government monitoring network is accredited by the National Association of Testing Authorities (NATA) for the measurement of all AAQ NEPM pollutants except SO2 as required under Clause 12 of the AAQ NEPM.

# ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL

For the purpose of this report, air quality is assessed against the AAQ NEPM standards and goals as specified in Schedule 2 of the AAQ NEPM and reproduced below in Table 3.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3, Table 3).

The goal of the AAQ NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specified in Schedule 2 of the AAQ NEPM. The extent is expressed as a maximum allowable number of exceedences for each standard (refer to column 4, Table 3). These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfires, which cannot be controlled through normal air quality management programs.

The AAQ NEPM also specifies advisory reporting standards for PM2.5. The goal for PM2.5 is to collect sufficient data to facilitate a review of the PM2.5 standards. This review is currently being undertaken as part of the broader AAQ NEPM review being undertaken EPHC.

Table 3: NEPM standards and goals

| Pollutant | Averaging Period | Maximum concentration | Goal within 10 years Maximum allowable exceedences |
| --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year none |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year none |
| Lead | 1 year | 0.050 μg/m3 | none |
| Particles as PM10 | 1 day | 50 μg/m3 | 5 days a year |
| Particles as PM2.5# | 1 day 1 year | 25 μg/m3 8 μg/m3 | Gather sufficient data nationally to facilitate a review of Advisory Reporting Standard. |

# - Reporting standard only

The following tables summarise compliance with the standards and goals of the AAQ NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded, the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

Air quality is assessed as complying with the AAQ NEPM if the number of exceedences of the standard is no more than the number specified in Schedule 2 of the AAQ NEPM and data availability was at least 75 percent in each quarter of the year.

Air quality is assessed as ‘not demonstrated’ if there has been insufficient data collected to demonstrate that the standards and goal have been met or not met.

## Carbon monoxide

During 2010, no exceedences of the CO standard were recorded in the ACT.

Table 4: 2010 compliance summary for CO AAQ NEPM standard - 9.0 ppm (8-hr average)

| Region/ Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra | 95.1 | 95.1 | 95.6 | 95.4 | 95.3 | 0 | Met |
| Monash |  |  |  |  |  |  |  |
| Civic | 94.4 | 94.5 | 95.5 | 95.7 | 95.0 | 0 | Met |

Monash

10

9

8

7

6

5

4

3

2

1

0

Figure 1: Daily max for CO 8-hr average - Monash

Civic

10

9

8

7

6

5

4

3

2

1

0

Figure 2: Daily max for CO 8-hr average - Civic

## Nitrogen dioxide

During 2010, no exceedences of the NO2 standard were recorded in the ACT. Compliance was not demonstrated for both Monash and Civic because all three NOx instruments failed with a period of a fortnight in Q1 and there were delays in getting the new parts in (refer to Table 5, Figure 3 and Figure 4).

Table 5: 2010 compliance summary for NO2

AAQ NEPM standard – 0.12 ppm (1 hour average), 0.03 ppm (1 year average)

| Region/ Performance monitoring station | Data availability rates (% of hours) | Annual mean Concentration (ppm) | Number of 1 hour exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 hour | 1 year |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |  |  |
| Canberra Monash Civic | 60.5 20.8 | 94.5 82.4 | 95.6 95.6 | 95.4 92.2 | 86.6 73.0 | 0.006 0.010 | 0 0 | ND ND | ND ND |

ND: Not demonstrated.

0.14

Monash

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 3: Daily max for NO2 - Monash

0.14

Civic

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 4: Daily max for NO2 – Civic

## Ozone

During 2010, no exceedences of the 1 hour and 4 hour standard for O3 were recorded in the ACT. Compliance was not demonstrated at Monash because of a lack of data in Q1. The low data availability rate was because of an error in the data logging systems which was not detected until April (refer to Table 6 and Figure 5).

Table 6: 2010 compliance summary for O3

AAQ NEPM standard – 0.10 ppm (1 hour average), 0.08 ppm (4 hour average)

| Region/ Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Canberra | 52.7 | 95.1 | 95.7 | 95.5 | 84.9 | 0 | 0 | ND | ND |
| Monash |  |  |  |  |  |  |  |  |  |
| Civic | 94.5 | 95.7 | 95.7 | 95.8 | 95.5 | 0 | 0 | Met | Met |

ND: Not demonstrated.

Monash

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 5: Daily max for 1 hour O3 – Monash

Civic

0.12

0.1

0.08

0.06

0.04

0.02

0

Figure 6: Daily max for 1 hour O3 – Civic

Monash

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

Figure 7: Daily max for 4 hours O3 - Monash

Civic

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

Figure 8: Daily max for 4 hours O3 - Civic

PM10

During 2010 there were no exceedences of the 24-hr PM10 standard recorded in the ACT. Monash complies with the 24-hr goal for PM10 but compliance was not demonstrated for Civic because of insufficient data in Q1 and Q2 (refer to Table 7 and Figure 10) with monitoring recommencing on 26 May following the installation of a Beta Attenuation Monitor.  Previous monitoring ceased in late 2008 because of instrument failure.

Table 7: 2010 compliance summary for PM10 AAQ NEPM standard 50 g/m3 1 day average

| Region/ Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra | 95.6 | 98.9 | 98.9 | 91.7 | 95.4 | 0 | Met |
| Monash |  |  |  |  |  |  |  |
| Civic | 0 | 40.7 | 98.9 | 94.2 | 57.9 | 0 | ND |

ND: Not demonstrated.

Monash

60

50

40

30

20

10

0

Figure 9: Daily max for PM10 – Monash.

Civic

60

50

40

30

20

10

0

Figure 10: Daily max for PM10 – Civic.

PM2.5

Two exceedences of the 24-hr advisory reporting standard were recorded on 19 and 20 March 2010 at Monash.  These exceedences were because of smoke from a number of large hazard reduction burns in NSW (near Tumut, Kosciusko NP and a few to the north and north-west of the ACT).

Table 8: 2010 compliance summary for PM2.5

AAQ NEPM standard – 25 g/m3 (1 day), 8 g/m3 (1year)

| Region/ Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration (g/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Canberra Monash | 98.9 | 98.9 | 95.7 | 89.3 | 95.1 | 6.7 | 2 |

Monash

60

50

40

30

20

10

0

Figure 11: Daily max for PM2.5 – Monash.

# ANALYSIS OF AIR QUALITY MONITORING

Annual summary statistics contained in Table 9 to Table 14 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The AAQ NEPM states that the short-term standards should not be exceeded on more than one day for CO, NO2, O3, and SO2 and on no more than five days per year for PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

## Carbon monoxide

Table 9: 2010 summary statistics for daily peak 8-hour CO AAQ NEPM standard - 9.0 ppm (8-hr average)

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 363 | 1.8 | 15 Jun 03:00 | 1.8 | 24 Jul 05:00 |
| Monash |  |  |  |  |  |
| Civic | 361 | 2.0 | 21 Jun 23:00 | 1.9 | 17 May 23:00 |

Carbon monoxide levels are well below the AAQ NEPM standard and because of both an improvement in vehicle emissions and a decline in wood heaters numbers, levels are trending down (refer to Figure 12 and Figure 13). The highest recorded value in the ACT during 2010 was 2.0ppm at Civic, which is only 22% of the standard.

## Nitrogen dioxide

Table 10: 2010 summary statistics for daily peak 1-hour NO2 AAQ NEPM standard 0.12 ppm (1 hour average)

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 326 | 0.037 | 19 Mar 20:00 | 0.034 | 11 Jan 21:00 |
| Monash |  |  |  |  |  |
| Civic | 274 | 0.039 | 1 Oct 19:00 | 0.037 | 15 Apr 18:00 |

Nitrogen dioxide levels are well below the AAQ NEPM standard and have remained stable over the last decade.  The highest recorded 1 hour value during 2010 was 0.039ppm at Civic.  This is only 32.5% of the standard. The highest recorded annual average in 2010 was 0.010ppm at Civic.  This is only 33.3% of the standard.

## Ozone

Table 11: 2010 summary statistics for daily peak 1-hour O3 AAQ NEPM standard 0.10 ppm (1-hour average)

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 317 | 0.051 | 6 Jan 18:00 | 0.050 | 11 Feb 18:00 |
| Monash |  |  |  |  |  |
| Civic | 363 | 0.058 | 27 Mar 14:00 | 0.054 | 22 Jan 11:00 |

Table 12: 2010 summary statistics for daily peak 4-hour O3 AAQ NEPM standard 0.08 ppm (4-hour average)

| Region/ Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 317 | 0.049 | 11 Feb 21:00 | 0.047 | 6 Jan 18:00 |
| Monash |  |  |  |  |  |
| Civic | 363 | 0.056 | 27 Mar 16:00 | 0.051 | 22 Jan 13:00 |

Ozone levels are below the AAQ NEPM standard. The highest recorded 1-hour value in the ACT during 2010 was 0.058ppm at Civic, which is 58% of the standard.  The highest recorded 4-hour value in the ACT during 2010 was 0.056ppm at Civic, which is 70% of the standard.

PM10

Table 13: 2010 summary statistics for daily peak PM10 AAQ NEPM standard 50 g/m3 (24-hour average)

| Region/ Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Canberra | 349 | 48.4 | 19 Mar | 28.0 | 26 Mar |
| Monash |  |  |  |  |  |
| Civic | 212 | 23.8 | 23 Nov | 15.6 | 26 Sept |

The highest PM10 level recorded during 2010 was 48.4μg/m3 on 19 March 2010 when there were a number of large hazard reduction burns in NSW. This is 96.8% of the AAQ NEPM standard.

PM2.5

Table 14: 2010 summary statistics for daily peak PM2.5 AAQ NEPM standard 25 g/m3 (24-hour average)

| Region/ Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Canberra Monash | 348 | 52.4 | 19 Mar | 21.6 | 16 May |

The 24-hour advisory reporting standard for PM2.5 was exceeded at Monash on 19 and 20 March 2010 (52.4μg/m3 and 27.5μg/m3 respectively) because of a number of large hazard reduction burns in NSW.

# ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL

The ACT is making steady progress towards achieving the goal of the AAQ NEPM, which is to achieve the standards specified in Schedule 2.

Historical monitoring indicates that the only AAQ NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions from domestic wood heaters. In more recent years exceedences of the particulate matter standard have also been recorded from dust storms and smoke from controlled burns.

Unfortunately compliance was “not demonstrated” for NO2 at Civic and Monash, O3 at Monash and PM10 at Civic because of less than 75 percent data availability in one or more quarters (see Monitoring Summary for more detail). With the exception of PM10 these pollutants are not of concern for the ACT airshed with levels of NO2 and O3 less than 33% and 70% of the standard respectively.

In relation to PM10 and PM2.5 it is pleasing to note that there were no exceedences of  either standard because of wood heater emissions, although monitoring clearly shows that levels increase during the winter months (refer to Figure 11 for details).  The two exceedences of the PM2.5 advisory reporting standard were because of smoke coming into the ACT airshed from controlled burns in NSW.

The ACT Government acknowledges that woodsmoke is a problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

It will continue to implement an integrated program to address woodsmoke.  This will involve public education and enforcement activities, the licensing of firewood merchants, the implementation of the ‘Don’t Burn Tonight Campaign’ and the on-going implementation of the Wood Heater Replacement Program.

The ACT will also work with the Commonwealth and other jurisdictions at a national level through the Standing Council on Environment and Water to progress actions to improve air quality.

# APPENDIX A: STATISTICAL SUMMARY AND TRENDS

The following section provides a basic statistical summary, using percentiles, for each station and for each standard. Percentiles for daily maximum values are presented.

## Carbon monoxide

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2001 – 2010

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 91.7 | 0 | 4.2 | 4.0 | 3.8 | 3.1 | 2.5 | 1.2 | 0.4 |
| 2002 | 92 | 0 | 4.3 | 3.7 | 3.4 | 2.9 | 2.3 | 1.2 | 0.4 |
| 2003 | 86.8 | 0 | 3.7 | 3.0 | 2.8 | 2.5 | 2.0 | 0.8 | 0.3 |
| 2004 | 94.1 | 0 | 3.2 | 2.7 | 2.5 | 2.0 | 1.6 | 0.9 | 0.5 |
| 2005 | 99.5 | 0 | 3.2 | 2.8 | 2.5 | 2.2 | 1.7 | 1.0 | 0.4 |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2010 | 99.2 | 0 | 1.8 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 12: Statistical summary for daily maximum 8-hour CO Monash 2001 – 2010

Table 16: Statistical summary for daily maximum 8-hour CO Civic 2001 – 2010

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 83.2 | 0 | 6.4 | 5.6 | 4.8 | 4.0 | 3.2 | 2.1 | 1.0 |
| 2002 | 86.8 | 0 | 5.1 | 4.7 | 4.4 | 3.52 | 2.9 | 1.6 | 0.6 |
| 2003 | 95.7 | 0 | 3.5 | 2.8 | 2.6 | 2.2 | 1.8 | 1.0 | 0.6 |
| 2004 | 95.7 | 0 | 4.6 | 3.6 | 3.2 | 2.3 | 1.6 | 0.6 | 0.6 |
| 2005 | 95.6 | 0 | 3.7 | 3.4 | 3.2 | 2.6 | 1.7 | 1.1 | 0.7 |
| 2006 | 95.4 | 0 | 2.8 | 2.7 | 2.6 | 2.1 | 1.4 | 0.8 | 0.5 |
| 2007 | 93.2 | 0 | 2.8 | 2.3 | 2.0 | 1.6 | 1.3 | 0.8 | 0.5 |
| 2008 | 92.7 | 0 | 2.3 | 2.1 | 2.0 | 1.6 | 1.2 | 0.7 | 0.4 |
| 2009 | 95.1 | 0 | 1.9 | 1.6 | 1.2 | 1.0 | 0.8 | 0.6 | 0.4 |
| 2010 | 98.6 | 0 | 2.0 | 1.9 | 1.8 | 1.4 | 1.2 | 0.9 | 0.6 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 13:  Statistical summary for daily maximum 8-hour CO Civic 2001 – 2010

## Nitrogen dioxide

Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 86.3 | 0 | 0.039 | 0.036 | 0.036 | 0.033 | 0.029 | 0.024 | 0.020 |
| 2002 | 88.3 | 0 | 0.045 | 0.036 | 0.034 | 0.031 | 0.026 | 0.022 | 0.017 |
| 2003 | 90.4 | 0 | 0.064 | 0.042 | 0.033 | 0.028 | 0.025 | 0.021 | 0.016 |
| 2004 | 91.8 | 0 | 0.040 | 0.033 | 0.031 | 0.028 | 0.026 | 0.022 | 0.018 |
| 2005 | 97.8 | 0 | 0.041 | 0.034 | 0.031 | 0.028 | 0.027 | 0.024 | 0.018 |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |
| 2010 | 89.1 | 0 | 0.037 | 0.029 | 0.028 | 0.025 | 0.023 | 0.021 | 0.017 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 14: Statistical summary for daily maximum 1-hour NO2 Monash 2001 – 2010

Table 18: Statistical summary for daily maximum 1-hour NO2 Civic 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 87.0 | 0 | 0.048 | 0.045 | 0.042 | 0.039 | 0.037 | 0.032 | 0.027 |
| 2002 | 88.2 | 0 | 0.062 | 0.050 | 0.044 | 0.038 | 0.034 | 0.029 | 0.024 |
| 2003 | 83.6 | 0 | 0.087 | 0.050 | 0.045 | 0.034 | 0.028 | 0.022 | 0.018 |
| 2004 | 88.3 | 0 | 0.042 | 0.037 | 0.035 | 0.030 | 0.027 | 0.022 | 0.018 |
| 2005 | 95.3 | 0 | 0.040 | 0.036 | 0.033 | 0.030 | 0.029 | 0.024 | 0.020 |
| 2006 | 95.2 | 0 | 0.044 | 0.035 | 0.034 | 0.031 | 0.028 | 0.022 | 0.018 |
| 2007 | 92.8 | 0 | 0.059 | 0.042 | 0.039 | 0.035 | 0.030 | 0.025 | 0.021 |
| 2008 | 88.6 | 0 | 0.046 | 0.037 | 0.035 | 0.033 | 0.030 | 0.026 | 0.020 |
| 2009 | 79.5 | 0 | 0.044 | 0.038 | 0.036 | 0.030 | 0.027 | 0.023 | 0.018 |
| 2010 | 74.9 | 0 | 0.039 | 0.035 | 0.033 | 0.030 | 0.027 | 0.024 | 0.021 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 15: Statistical summary for daily maximum 1-hour NO2 Civic 2001 – 2010

0.035

0.025

0.02

0.015

0.01

0.005

0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 16: Annual average 1-hour NO2 Monash 2001 – 2010

0.035

0.03

0.025

0.02

0.015

0.01

0.005

0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 17: Annual average 1-hour NO2 Civic 2001 – 2010

## Ozone

Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 81.5 | 0 | 0.062 | 0.044 | 0.041 | 0.038 | 0.034 | 0.030 | 0.026 |
| 2002 | 93.5 | 0 | 0.063 | 0.055 | 0.052 | 0.047 | 0.042 | 0.032 | 0.024 |
| 2003 | 92.4 | 0 | 0.102 | 0.069 | 0.061 | 0.050 | 0.045 | 0.035 | 0.025 |
| 2004 | 94.1 | 0 | 0.064 | 0.56 | 0.054 | 0.048 | 0.044 | 0.038 | 0.030 |
| 2005 | 97.8 | 0 | 0.065 | 0.058 | 0.053 | 0.045 | 0.041 | 0.034 | 0.030 |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |
| 2010 | 86.6 | 0 | 0.051 | 0.048 | 0.046 | 0.042 | 0.037 | 0.033 | 0.030 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 18: Statistical summary for daily maximum 1-hour O3 Monash 2001 – 2010

Table 20: Statistical summary for daily maximum 1-hour O3 Civic 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 88.3 | 0 | 0.055 | 0.050 | 0.046 | 0.043 | 0.040 | 0.035 | 0.028 |
| 2002 | 79.8 | 0 | 0.082 | 0.060 | 0.053 | 0.049 | 0.044 | 0.035 | 0.029 |
| 2003 | 93.6 | 0 | 0.094 | 0.065 | 0.055 | 0.049 | 0.045 | 0.037 | 0.031 |
| 2004 | 93.5 | 0 | 0.071 | 0.055 | 0.053 | 0.045 | 0.041 | 0.034 | 0.028 |
| 2005 | 85.5 | 0 | 0.070 | 0.061 | 0.051 | 0.042 | 0.038 | 0.032 | 0.028 |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |
| 2010 | 99.2 | 0 | 0.058 | 0.050 | 0.048 | 0.040 | 0.036 | 0.029 | 0.025 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 19: Statistical summary for daily maximum 1-hour O3 Civic 2001 – 2010

Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 81.5 | 0 | 0.051 | 0.041 | 0.038 | 0.035 | 0.032 | 0.028 | 0.024 |
| 2002 | 93.5 | 0 | 0.058 | 0.051 | 0.049 | 0.044 | 0.039 | 0.031 | 0.023 |
| 2003 | 92.4 | 1 | 0.082 | 0.063 | 0.058 | 0.048 | 0.043 | 0.033 | 0.025 |
| 2004 | 94.1 | 0 | 0.060 | 0.053 | 0.051 | 0.045 | 0.042 | 0.036 | 0.029 |
| 2005 | 97.5 | 0 | 0.062 | 0.054 | 0.049 | 0.044 | 0.039 | 0.033 | 0.029 |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |
| 2010 | 86.6 | 0 | 0.049 | 0.046 | 0.043 | 0.040 | 0.037 | 0.032 | 0.029 |

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 20: Statistical summary for daily maximum 4-hour O3 Monash 2001 – 2010

Table 22: Statistical summary for daily maximum 4-hour O3 Civic 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 88.3 | 0 | 0.048 | 0.045 | 0.043 | 0.041 | 0.038 | 0.032 | 0.026 |
| 2002 | 79.8 | 0 | 0.073 | 0.057 | 0.051 | 0.046 | 0.042 | 0.033 | 0.027 |
| 2003 | 93.6 | 0 | 0.078 | 0.055 | 0.051 | 0.046 | 0.042 | 0.036 | 0.029 |
| 2004 | 93.5 | 0 | 0.062 | 0.052 | 0.048 | 0.043 | 0.039 | 0.32 | 0.026 |
| 2005 | 85.5 | 0 | 0.061 | 0.054 | 0.047 | 0.040 | 0.036 | 0.031 | 0.026 |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |
| 2010 | 99.2 | 0 | 0.056 | 0.047 | 0.044 | 0.037 | 0.034 | 0.028 | 0.024 |

0.090

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 21: Statistical summary for daily maximum 4-hour O3 Civic 2001 – 2010

PM10

Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 15.9 | 4 | 70.6 | 66.1 | 61.9 | 56.2 | 45.6 | 25.0 | 13.9 |
| 2002 | 75 | 0 | 108.4 | 56.6 | 48.5 | 42.4 | 37.7 | 25.3 | 16.2 |
| 2003 | 97.5 | 13 | 350.4 | 136.4 | 105.3 | 39.6 | 30.3 | 21.2 | 14.6 |
| 2004 | 99.7 | 3 | 52.0 | 48.2 | 46.0 | 33.8 | 28.5 | 20.7 | 14.7 |
| 2005 | 97.5 | 10 | 98.8 | 57.6 | 52.7 | 37.3 | 31.0 | 21.2 | 14.5 |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |
| 2010 | 95.4 | 0 | 48.4 | 35.6 | 27.4 | 23.5 | 20.2 | 14.7 | 10.0 |

60

50

40

30

20

10

0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 22: Statistical summary for daily maximum 24-hour PM10 Monash 2001 – 2010

Note 2009 data has not been included in Figure 22 as the percentile data has been skewed because of insufficient data in Q1 and Q2 (zero and twenty five percent respectively) and the extreme readings associated with the dust storm which affected most of eastern Australia on 22 and 23 September, 2009.

Table 24: Statistical summary for daily maximum 24-hour PM10 Civic 2001 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2001 | 14.8 | 0 | 33..6 | 33.3 | 32.7 | 27.5 | 26.2 | 20.8 | 16.2 |
| 2002 | 15.6 | 3 | 67.4 | 67.1 | 66.3 | 42.7 | 25.4 | 18.7 | 15.3 |
| 2003 | 12.6 | 0 | 20.8 | 20.8 | 20.7 | 19.3 | 17.3 | 13.6 | 9.3 |
| 2004 | 16.7 | 0 | 33.2 | 32.4 | 32.0 | 28.1 | 22.5 | 17.9 | 14.4 |
| 2005 | 9.6 | 1 | 50.64 | 47.2 | 43.8 | 34.8 | 27.5 | 19.5 | 12.7 |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |
| 2009 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 2010 | 57.6 | 0 | 23.8 | 19.7 | 17.1 | 14.7 | 13.7 | 11.1 | 8.4 |

60.0

50.0

40.0

30.0

20.0

10.0

0.0

2001	2002	2003	2004	2005	2006	2007	2008	2009	2010

Figure 23: Statistical summary for daily maximum 24-hour PM10 Civic 2001 – 2010

Note No PM10 monitoring was conducted at Civic in 2009.

PM2.5

Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2010

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.1 | 15 | 38.3 | 35.8 | 31.5 | 23.5 | 16.6 | 9.5 | 6.2 |
| 2005 | 73.6 | 14 | 38.6 | 31.4 | 29.3 | 25.0 | 20.7 | 9.0 | 4.9 |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |
| 2010 | 95.1 | 2 | 52.4 | 22.1 | 20.9 | 17.4 | 14.3 | 7.8 | 4.4 |

30.0

25.0

20.0

15.0

10.0

5.0

0.0

2004	2005	2006	2007	2008	2009	2010

Figure 24: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2010

10

9

7

6

5

4

3

2

1

0

2004	2005	2006	2007	2008	2009	2010

Figure 25: Annual average 24-hour PM2.5 Monash 2004 - 2010

# Text boxes

Term	Definition

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

part per million

NEPM standard

part per million

NEPM standard

part per million

NEPM standard

part per million

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

micrograms per cubic metre

NEPM standard

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre

NEPM Standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

NEPM standard

parts per million

NEPM standard

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile 75 %ile 50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

NEPM Standard

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM advisory standard

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre