ACT Air Quality Report 2013

Environment Protection Authority

JUNE 2014

© Australian Capital Territory, Canberra 2014

This work is copyright. Apart from any use as permitted under the Copyright Act 1968,

no part may be reproduced by any process without written permission from:

Director-General, Environment and Planning Directorate, ACT Government, GPO Box 158, Canberra, ACT 2601

Telephone: 02 6207 1923 Website:www.environment.act.gov.au

Printed on recycled paper

### ACCESSIBILITY

The ACT Government is committed to making its informati	services, events and venues as accessible as possible.

If you have diffi	reading a standard printed document and would like to receive this publicati	in an alternati e format, such as large print, please phone Canberra Connect on 13 22 81 or email the Environment and Planning Directorate at epd_communicati	gov.au

If English is not your fi st language and you require a translati	and interpreti	service, please phone 13 14 50. If you are deaf, or have a speech or hearing impairment, and need the teletypewriter service, please phone

13 36 77 and ask for Canberra Connect on 13 22 81.

For speak and listen users, please phone 1300 555 727 and ask for Canberra Connect on 13 22 81. For more informati	on these services visit htt	ww.relayservice.com.au

### List of definitions and abbreviations	2

Overview	3

Monitoring summary	4

Current Performance Monitoring Stations	4

Monitoring Methods	4

NATA Accreditation Status	4

### Assessment of compliance with standards and 2008 goal	5

Carbon monoxide	6

Nitrogen dioxide	7

Ozone	8

PM10	10

PM2.5	11

### Analysis of air quality monitoring	12

Carbon monoxide	12

Nitrogen dioxide	12

Ozone	12

PM10	13

PM2.5	13

### Assessment of progress towards achieving the goal	14

Appendix A: Statistical summary and trends	15

Carbon monoxide	15

Nitrogen dioxide	17

Ozone	20

PM10	24

PM2.5	26

AAQ NEPM  National Environment Protection (Ambient Air Quality) Measure

ACT	Australian Capital Territory

CO	Carbon Monoxide

BAM	Beta Attenuation Monitor

NATA	National Association of Testing Authorities ND	Not Demonstrated

NO2	Nitrogen Dioxide

O3	Ozone

PMS	Performance Monitoring Station

PM2.5	Particles with an equivalent aerodynamic diameter less than or equal to 2.5 Micrometers PM10	Particles with an equivalent aerodynamic diameter less than or equal to 10 Micrometers ppm	Parts per million by volume – parts of pollutant per million parts of air

Q	Quarter (e.g. Q1 means the first quarter of the year) SO2	Sulfur Dioxide

µg/m3	micrograms per cubic metre

This report presents the results of ambient air quality monitoring in the ACT for the 2013 calendar year and assesses them in accordance with the requirements of the National Environment Protection (Ambient Air Quality) Measure (AAQ NEPM) which was made by the National Environment Protection Council on 26 June 1998.

The AAQ NEPM establishes:

- requirements for monitoring air quality;

- air quality standards that are levels of specifi	pollutants against which air quality can be assessed; and

- a goal that the air quality standards be met to the extent specifi	in the NEPM. Recognising that certain events can impact on air quality, the NEPM specifi	a maximum number of days on which it is permissible to exceed the standard.

The ACT monitors four of the six NEPM pollutants, namely carbon monoxide (CO), nitrogen dioxide (NO2), photochemical oxidants as ozone (O3) and particulate matter (particles less than 10 microns in diameter – PM10 and particles less than 2.5 microns – PM2.5). Due to a lack of heavy industry, the ACT has never monitored sulfur dioxide (SO2) as it is primarily an industrial pollutant, and lead monitoring ceased in 2002 with the phase out of leaded petrol. Monitoring was performed in accordance with the ACT’s monitoring plan, AAQ NEPM Technical Papers and ACT Health’s accreditation by the National Association of Testing Authorities (NATA).

Monitoring results demonstrate that Canberra’s air quality is excellent compared to other capital cities, with no exceedences of the AAQ NEPM standards for CO, NO2, and O3. The major impacts on Canberra’s air quality in 2013, as in previous years, came from the accumulation of combustion particles from wood heaters in cold, highly stable air and hazard reduction burns.

One exceedence of the PM10 24-hour standard was measured on 19 October at the Civic station. The cause of this exceedence was a controlled burn in NSW. There were six exceedences of the PM2.5   24-hour advisory reporting standard measured at Monash. Four exceedences occurred between May and July and can be

attributed to domestic wood heater emissions. Two exceedences occurred on 19 and 20 October due to smoke coming from a hazard reduction burn in NSW.

The ACT Government acknowledges that woodsmoke from domestic wood heaters is the largest source of air pollution in Canberra and has implemented a range of programs to address it. The monitoring results show that these programs have been effective in reducing woodsmoke with particle levels continuing to trend down.

## Current Performance Monitoring Stations

The ACT Government has been undertaking ambient air quality monitoring in Canberra since the early 1990’s. The Health Directorate is responsible for the Government’s ambient air quality monitoring network. The Environment and Planning Directorate is responsible for annual reporting under the AAQ NEPM.

The AAQ NEPM monitoring network in the ACT currently consists of two monitoring stations at Monash and Civic respectively. The Monash station is approximately 300 metres west of Cockcroft Avenue in the Monash District Playing Fields. The Civic station is located at the northern end of the carpark on the western side of the Olympic Swimming Pool adjacent to Allara Street. The compliance and non-compliance criteria for both stations against the siting standard AS/NZS 3580.1.1:2007 are listed in Table 1 below.

### Table 1 Summary of stations’ siting compliance with AS 3580.1.1:2007

| Station | Height above ground | Minimum distance to support structure | Clear sky angle of 120° | Unrestricted airflow of 270°/360° | 20m from trees | No boilers or incinerators nearby | Minimum distance from road or traffic |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Monash |  |  |  |  |  |  |  |
| Civic |  |  |  |  |  |  |  |

During this reporting period the ACT Government established another performance monitoring station (PMS) in Florey. The new station has been operational since 28 February 2014 and is fully compliant with the AAQ NEPM. Data from this station will be used for the 2014 annual report.

Both Monash and Civic stations contain instrumentation that continuously monitors CO, O3, NO2 and PM10. The monitoring of PM2.5 is only undertaken at Monash.

## Monitoring Methods

The ACT monitoring is conducted in accordance with the relevant Australian Standards as shown in Table 2.

Data not meeting the requirements of these Standards are identified as invalid and not included in this report.

### Table 2 Methods used for monitoring AAQ NEPM pollutants

| Pollutant | Standard | Title | Method Used |
| --- | --- | --- | --- |
| Carbon Monoxide | AS 3580.7.1-2011 | Ambient Air – Determination of Carbon Monoxide – Direct Reading Instrument Method | Gas filter correlation/Infrared |
| Nitrogen dioxide | AS 3580.5.1-2011 | Ambient Air – Determination of Oxides of Nitrogen – Chemiluminescence Method | Gas phase chemiluminescence |
| Photochemical oxidant (ozone) | AS 3580.6.1-2011 | Ambient Air – Determination of Ozone – Direct Reading Instrument Method | Non-dispersive ultraviolet |
| PM10 | AS 3580.9.11-2008 | Method for Sampling and Analysis of ambient air Method – Determination of suspended particles matter – PM10 beta attenuation monitors | Beta Attenuation Monitor (BAM) |
| PM10 | AS/NZS 3580.9.6- 2004 | Methods for sampling and analysis of ambient air- Determination of suspended particulate matter- PM10 high volume sampler with size- selective inlet- Gravimetric method | Gravimetric Reference Method |
| PM2.5 | AS/NZS 3580.9.10- 2006 | Reference Method for the Determination of Fine Particulate matter as PM2.5 in the Atmosphere | Gravimetric Reference Method |

NATA Accreditation Status

The ACT Government monitoring network is accredited by NATA for the measurement of all AAQ NEPM pollutants except SO2 as required under Clause 12 of the AAQ NEPM.

# Assessment of compliance with standards and 2008 goal

For the purpose of this report, air quality is assessed against the AAQ NEPM standards and goals as specified in Schedule 2 of the AAQ NEPM and reproduced in Table 3.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3, Table 3).

The goal of the AAQ NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specifi	in Schedule 2 of the AAQ NEPM. The extent is expressed as a maximum allowable number of exceedences for each standard (refer to column 4, Table 3).

These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfi es, which cannot be controlled through normal air quality management programs.

The AAQ NEPM also specifi	advisory reporting standards for PM2.5. The goal for PM2.5 is to collect suffi	t data to facilitate a review of the PM2.5 standards, which has been completed through the review of the AAQ NEPM.

### Table 3: AAQ NEPM standards and goals

| Pollutant | Averaging period | Maximum concentration | Goal within 10 years Maximum allowable exceedences |
| --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year none |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year none |
| Lead | 1 year | 0.050 μg/m3 | none |
| Particles as PM10 | 1 day | 50 μg/m3 | 5 days a year |
| Particles as PM # 2.5 | 1 day 1 year | 25 μg/m3 8 μg/m3 | Not applicable Not applicable |

#- Advisory reporting standards only

The following tables (Table 4 to Table 8) summarise compliance with the standards and goals of the AAQ NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded; the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

A station’s performance is assessed as complying with the AAQ NEPM (i.e. ’MET’) if the number of exceedences is no more than the number specified in Schedule 2 of the AAQ NEPM and data availability was at least 75% in each quarter of the year. A region demonstrates compliance with the AAQ NEPM when either all stations in the region demonstrate compliance, or when the region meets approved pollutant screening criteria.

A station’s performance is assessed as not complying with the AAQ NEPM (i.e. ‘NOT MET’) if there is more than the number of exceedences specified in Schedule 2 of the AAQ NEPM, even if the data availability rates are less than the 75% required.

A station’s performance is assessed as ‘NOT DEMONSTRATED’ (ND) if it records exceedences on a number of days less than that allowed, but has data availability rates less than 75% in any quarter. This may be due to instrument failures, temporary closures for upgrading or closures to allow relocation of the station.

These categories (i.e. MET, NOT MET and ND) are used in the tables on the following pages.

Carbon monoxide

During 2013, no exceedences of the CO standard were recorded in the ACT and compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 4: 2013 compliance summary for CO

AAQ NEPM standard- 9.0 ppm (8-hour average)

| Performance monitoring station |  | Data availability rates (% of hours) |  | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash Civic | 93.6 95.6 | 90.0 95.0 | 95.6 95.1 | 95.1 92.7 |  | 93.6 94.6 | 0 0 | MET MET |

Figure 1: Daily max for CO 8-hour average - Monash

Figure 2: Daily max for CO 8-hour average - Civic

## Nitrogen dioxide

During 2013, no exceedences of the NO2 standards were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 5: 2013 compliance summary for NO2

AAQ NEPM standard – 0.12 ppm (1-hour average), 0.03 ppm (1-year average)

| Performance monitoring station | Data availability rates (% of hours) | Annual mean Concentration (ppm) | Number of 1 hour exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  | 1 hour | 1 year |
| Monash Civic | 94.5 95.6 | 90.3 95.0 | 95.6 94.1 | 95.1 92.7 | 93.9 94.3 | 0.005 0.007 | 0 0 | MET MET | MET MET |

Figure 3: Daily max for NO2 – Monash

Figure 4: Daily max for NO2 – Civic

## Ozone

During 2013, no exceedences of the 1-hour and 4-hour standards for O3 were recorded in the ACT, and compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 6: 2013 compliance summary for O3

AAQ NEPM standard – 0.10 ppm (1-hour average), 0.08 ppm (4-hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Monash Civic | 94.6 76.3 | 90.8 90.7 | 95.5 95.4 | 95.8 92.3 | 94.2 88.7 | 0 0 | 0 0 | MET MET | MET MET |

Figure 5: Daily max for 1 hour O3 – Monash

Figure 6: Daily max for 1 hour O3 – Civic

Figure 7: Daily max for 4 hours O3 - Monash

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

Figure 8: Daily max for 4 hours O3 - Civic

0.09

0.08

0.07

0.06

0.05

0.04

0.03

0.02

0.01

0

10

During 2013, there was one exceedence of the 24-hour PM10 standard recorded at Civic. Compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 7: 2013 compliance summary for PM10

AAQ NEPM standard 50 µg/m3 1-day average

| Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash Civic | 95.6 83.3 | 93.4 100 | 90.3 98.4 | 100 91.8 | 95.6 92.9 | 0 1 | MET MET |

Figure 9: Daily max for PM10 – Monash

Figure 10: Daily max for PM10 – Civic

2.5

Six exceedences of the 24-hour advisory reporting standard were recorded at Monash during 2013.

Table 8: 2013 compliance summary for PM2.5

AAQ NEPM standard – 25 µg/m3 (1-day), 8 µg/m3 (1-year)

| Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration (µg/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 100 | 95.6 | 98.4 | 100 | 98.6 | 6.9 | 6 |

Figure 11: Daily max for PM2.5 – Monash

45.0

40.0

35.0

30.0

25.0

20.0

15.0

10.0

5.0

0.0

# Analysis of air quality monitoring

Annual summary statistics contained in Table 9 to Table 14 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The AAQ NEPM states that the short-term standards should not be exceeded on more than one day for CO, NO2 and O3, and on no more than five days per year for PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

## Carbon monoxide

### Table 9: 2013 summary statistics for daily peak 8-hour CO

AAQ NEPM standard- 9.0 ppm (8-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 350 357 | 2.1 1.5 | 22 Jun 04:00 21 Jun 23:00 | 2.1 1.4 | 22 Jun 03:00 21 Jun 00:00 |

Carbon monoxide levels are well below the AAQ NEPM standard. The highest recorded value in the ACT during 2013 was 2.1ppm at Monash, where levels reached 23% of the standard.

## Nitrogen dioxide

### Table 10: 2013 summary statistics for daily peak 1-hour NO2

AAQ NEPM standard 0.12 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 357 358 | 0.037 0.045 | 17 Jan 21:00 19 Oct 20:00 | 0.035 0.040 | 07 Jan 21:00 09 May 18:00 |

Nitrogen dioxide levels are well below the AAQ NEPM standard and have remained stable over the last decade. The highest recorded 1-hour value during 2013 was 0.045ppm at Civic, which is only 38% of the standard. The highest recorded annual average in 2013 was 0.007ppm at Civic. This is 23% of the annual standard 0.03ppm.

## Ozone

### Table 11: 2013 summary statistics for daily peak 1-hour O3

AAQ NEPM standard 0.10 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 357 336 | 0.062 0.060 | 19 Oct 18:00 19 Oct 18:00 | 0.053 0.047 | 17 Jan 12:00 07 Mar 14:00 |

### Table 12: 2013 summary statistics for daily peak 4-hour O3

AAQ NEPM standard 0.08 ppm (4-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 357 335 | 0.059 0.057 | 19 Oct 18:00 19 Oct 18:00 | 0.050 0.045 | 06 Jan 14:00 07 Mar 16:00 |

Ozone levels are below the AAQ NEPM standard. The highest recorded 1-hour value in the ACT during 2013 was 0.062ppm at Monash, which is 62% of the standard. The highest recorded 4-hour value in the ACT during 2013 was 0.059ppm at Monash. This is 74% of the standard.

10

### Table 13: 2013 summary statistics for daily peak PM10

AAQ NEPM standard 50 µg/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (µg/m3) | Highest (date) | 6th Highest (µg/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 349 339 | 43.5 57.8 | 20 October 19 October | 25.3 25.3 | 10 January 27 October |

PM10 levels are below the AAQ NEPM standard. The highest PM10 level recorded during 2013 was 57.8μg/m  at

Civic on 19 October 2013. This is due to a hazard reduction burn in NSW.

2.5

### Table 14: 2013 summary statistics for daily peak PM2.5

AAQ NEPM standard 25 µg/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (µg/m3) | Highest (date) | 6th Highest (µg/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash | 360 | 38.4 | 20 October | 27.2 | 28 July |

The 24-hour advisory reporting standard for PM2.5 was exceeded six times at Monash. Four exceedences occurred between May and July and can be attributed to domestic wood heater emissions. Two exceedences occurred on 19 and 20 October respectively due to smoke coming from a hazard reduction burn in NSW.

# Assessment of progress towards achieving the goal

The ACT is currently compliant with the goal specified in Schedule 2 of the AAQ NEPM.

Historical monitoring results indicate that the only AAQ NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions from domestic wood heaters. In more recent years exceedences of the particulate matter standards have also been attributed to dust storms and smoke from controlled burns.

The ACT Government acknowledges that woodsmoke is a problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

It will continue to implement an integrated program to address woodsmoke. This will involve public education and enforcement activities, the licensing of firewood merchants, the implementation of the ‘Don’t Burn Tonight Campaign’ and ‘Burn Right Tonight Campaign’, and the on-going administration of the Wood Heater Replacement Program.

The ACT is also working with the Commonwealth and other jurisdictions at a national level to progress actions to improve air quality. At the Environment Ministers Meeting on 29 April 2014, Ministers signalled their intention to vary the AAQ NEPM for particles reflecting the latest scientific understanding on health risks arising from particle pollution. The Measure seeks to establish a more stringent reporting standard for

particle pollution (PM2.5 and PM10). An Impact Statement on the proposed variation will be released for public consultation following the completion of statutory processes.

Reflecting the significance of fine particle emissions from ‘non-road spark ignition engines’ (marine engines and garden equipment) and wood heaters, Ministers requested finalisation, by September 2014, of Decision Regulation Impact Statements on potential emission control options for these sectors.

# Appendix A: Statistical summary and trends

The following section provides a basic statistical summary, using percentiles, for each station and for each standard. Percentiles for daily maximum values are presented.

## Carbon monoxide

### Table 15: Statistical summary for daily maximum 8-hour CO Monash 2004 – 2013

| Year | Data Avail. (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 94.1 | 0 | 3.2 | 2.7 | 2.5 | 2.0 | 1.6 | 0.9 | 0.5 |
| 2005 | 99.5 | 0 | 3.2 | 2.8 | 2.5 | 2.2 | 1.7 | 1.0 | 0.4 |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2010 | 99.2 | 0 | 1.8 | 1.7 | 1.6 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2011 | 98.6 | 0 | 2.2 | 1.9 | 1.8 | 1.5 | 1.1 | 0.5 | 0.2 |
| 2012 | 99.7 | 0 | 1.8 | 1.7 | 1.7 | 1.2 | 1.0 | 0.6 | 0.3 |
| 2013 | 95.9 | 0 | 2.1 | 1.9 | 1.8 | 1.5 | 1.2 | 0.6 | 0.3 |

Figure 12: Stati ti al summary for daily maximum 8-hour CO Monash 2004 – 2013

10.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

### Table 16: Statistical summary for daily maximum 8-hour CO Civic 2004 – 2013

| Year | Data Avail. (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 95.7 | 0 | 4.6 | 3.6 | 3.2 | 2.3 | 1.6 | 0.6 | 0.6 |
| 2005 | 95.6 | 0 | 3.7 | 3.4 | 3.2 | 2.6 | 1.7 | 1.1 | 0.7 |
| 2006 | 95.4 | 0 | 2.8 | 2.7 | 2.6 | 2.1 | 1.4 | 0.8 | 0.5 |
| 2007 | 93.2 | 0 | 2.8 | 2.3 | 2.0 | 1.6 | 1.3 | 0.8 | 0.5 |
| 2008 | 92.7 | 0 | 2.3 | 2.1 | 2.0 | 1.6 | 1.2 | 0.7 | 0.4 |
| 2009 | 95.1 | 0 | 1.9 | 1.6 | 1.2 | 1.0 | 0.8 | 0.6 | 0.4 |
| 2010 | 98.6 | 0 | 2.0 | 1.9 | 1.8 | 1.4 | 1.2 | 0.9 | 0.6 |
| 2011 | 97.8 | 0 | 2.0 | 1.8 | 1.6 | 1.4 | 1.0 | 0.7 | 0.5 |
| 2012 | 95.9 | 0 | 1.8 | 1.5 | 1.4 | 1.3 | 1.1 | 0.7 | 0.4 |
| 2013 | 97.8 | 0 | 1.5 | 1.3 | 1.1 | 1.0 | 0.8 | 0.5 | 0.3 |

Figure 13: Stati ti al summary for daily maximum 8-hour CO Civic 2004 – 2013

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

## Nitrogen dioxide

### Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2004 – 2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 91.8 | 0 | 0.040 | 0.033 | 0.031 | 0.028 | 0.026 | 0.022 | 0.018 |
| 2005 | 97.8 | 0 | 0.041 | 0.034 | 0.031 | 0.028 | 0.027 | 0.024 | 0.018 |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |
| 2010 | 89.1 | 0 | 0.037 | 0.029 | 0.028 | 0.025 | 0.023 | 0.021 | 0.017 |
| 2011 | 96.7 | 0 | 0.043 | 0.031 | 0.030 | 0.029 | 0.026 | 0.022 | 0.015 |
| 2012 | 97.5 | 0 | 0.033 | 0.030 | 0.029 | 0.026 | 0.025 | 0.021 | 0.014 |
| 2013 | 97.5 | 0 | 0.037 | 0.031 | 0.030 | 0.027 | 0.025 | 0.021 | 0.014 |

Figure 14: Stati ti al summary for daily maximum 1-hour NO2 Monash 2004 – 2013

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

Figure 15: Annual average 1-hour NO2 Monash 2004 – 2013

0.035

0.025

0.020

0.015

0.010

0.005

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

### Table 18: Statistical summary for daily maximum 1-hour NO2 Civic 2004 – 2013

| Year | Data Recovery (%) | No. of exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 88.3 | 0 | 0.042 | 0.037 | 0.035 | 0.030 | 0.027 | 0.022 | 0.018 |
| 2005 | 95.3 | 0 | 0.040 | 0.036 | 0.033 | 0.030 | 0.029 | 0.024 | 0.020 |
| 2006 | 95.2 | 0 | 0.044 | 0.035 | 0.034 | 0.031 | 0.028 | 0.022 | 0.018 |
| 2007 | 92.8 | 0 | 0.059 | 0.042 | 0.039 | 0.035 | 0.030 | 0.025 | 0.021 |
| 2008 | 88.6 | 0 | 0.046 | 0.037 | 0.035 | 0.033 | 0.030 | 0.026 | 0.020 |
| 2009 | 79.5 | 0 | 0.044 | 0.038 | 0.036 | 0.030 | 0.027 | 0.023 | 0.018 |
| 2010 | 74.9 | 0 | 0.039 | 0.035 | 0.033 | 0.030 | 0.027 | 0.024 | 0.021 |
| 2011 | 88.8 | 0 | 0.046 | 0.036 | 0.035 | 0.032 | 0.029 | 0.023 | 0.018 |
| 2012 | 98.6 | 0 | 0.044 | 0.036 | 0.033 | 0.030 | 0.029 | 0.024 | 0.019 |
| 2013 | 98.1 | 0 | 0.045 | 0.038 | 0.036 | 0.033 | 0.029 | 0.022 | 0.016 |

Figure 16: Stati ti al summary for daily maximum 1-hour NO2 Civic 2004 – 2013

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

Figure 17: Annual average 1-hour NO2 Civic 2004 – 2013

0.035

0.030

0.025

0.020

0.015

0.010

0.005

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

## Ozone

### Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2004 – 2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 94.1 | 0 | 0.064 | 0.56 | 0.054 | 0.048 | 0.044 | 0.038 | 0.030 |
| 2005 | 97.8 | 0 | 0.065 | 0.058 | 0.053 | 0.045 | 0.041 | 0.034 | 0.030 |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |
| 2010 | 86.6 | 0 | 0.051 | 0.048 | 0.046 | 0.042 | 0.037 | 0.033 | 0.030 |
| 2011 | 99.2 | 0 | 0.056 | 0.052 | 0.047 | 0.044 | 0.040 | 0.033 | 0.028 |
| 2012 | 100 | 0 | 0.055 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.062 | 0.051 | 0.049 | 0.045 | 0.041 | 0.035 | 0.029 |

Figure 18: Stati ti al summary for daily maximum 1-hour O3 Monash 2004 – 2013

0.120

0.080

0.060

0.040

0.020

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.5 | 0 | 0.071 | 0.055 | 0.053 | 0.045 | 0.041 | 0.034 | 0.028 |
| 2005 | 85.5 | 0 | 0.070 | 0.061 | 0.051 | 0.042 | 0.038 | 0.032 | 0.028 |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |
| 2010 | 99.2 | 0 | 0.058 | 0.050 | 0.048 | 0.040 | 0.036 | 0.029 | 0.025 |
| 2011 | 96.4 | 0 | 0.052 | 0.046 | 0.045 | 0.041 | 0.036 | 0.030 | 0.026 |
| 2012 | 100 | 0 | 0.053 | 0.041 | 0.038 | 0.034 | 0.030 | 0.024 | 0.020 |
| 2013 | 92.1 | 0 | 0.060 | 0.043 | 0.041 | 0.036 | 0.032 | 0.028 | 0.024 |

Figure 19: Stati ti al summary for daily maximum 1-hour O3 Civic 2004 – 2013

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

### Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2004 – 2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 94.1 | 0 | 0.060 | 0.053 | 0.051 | 0.045 | 0.042 | 0.036 | 0.029 |
| 2005 | 97.5 | 0 | 0.062 | 0.054 | 0.049 | 0.044 | 0.039 | 0.033 | 0.029 |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |
| 2010 | 86.6 | 0 | 0.049 | 0.046 | 0.043 | 0.040 | 0.037 | 0.032 | 0.029 |
| 2011 | 98.9 | 0 | 0.054 | 0.048 | 0.044 | 0.041 | 0.038 | 0.032 | 0.027 |
| 2012 | 99.7 | 0 | 0.052 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.059 | 0.048 | 0.047 | 0.042 | 0.039 | 0.033 | 0.028 |

Figure 20: Stati ti al summary for daily maximum 4-hour O3 Monash 2004 – 2013

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.5 | 0 | 0.062 | 0.052 | 0.048 | 0.043 | 0.039 | 0.32 | 0.026 |
| 2005 | 85.5 | 0 | 0.061 | 0.054 | 0.047 | 0.040 | 0.036 | 0.031 | 0.026 |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |
| 2010 | 99.2 | 0 | 0.056 | 0.047 | 0.044 | 0.037 | 0.034 | 0.028 | 0.024 |
| 2011 | 96.4 | 0 | 0.050 | 0.044 | 0.041 | 0.038 | 0.035 | 0.029 | 0.025 |
| 2012 | 100 | 0 | 0.042 | 0.037 | 0.036 | 0.032 | 0.028 | 0.023 | 0.019 |
| 2013 | 91.8 | 0 | 0.057 | 0.040 | 0.038 | 0.034 | 0.030 | 0.027 | 0.023 |

Figure 21: Stati ti al summary for daily maximum 4-hour O3 Civic 2004 – 2013

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

10

### Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2004 – 2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 99.7 | 3 | 52.0 | 48.2 | 46.0 | 33.8 | 28.5 | 20.7 | 14.7 |
| 2005 | 97.5 | 10 | 98.8 | 57.6 | 52.7 | 37.3 | 31.0 | 21.2 | 14.5 |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |
| 2010 | 95.4 | 0 | 48.4 | 35.6 | 27.4 | 23.5 | 20.2 | 14.7 | 10.0 |
| 2011 | 99.2 | 0 | 40.0 | 33.7 | 30.3 | 22.8 | 18.6 | 13.2 | 8.7 |
| 2012 | 98.6 | 0 | 41.0 | 24.2 | 21.8 | 19.7 | 17.4 | 13.7 | 9.7 |
| 2013 | 95.6 | 0 | 43.5 | 29.1 | 25.1 | 20.2 | 16.8 | 13.1 | 8.9 |

Figure 22: Stati ti al summary for daily maximum 24-hour PM10 Monash 2004 – 2013

60.0

50.0

40.0

30.0

20.0

10.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

Note 2009 data has not been included in Figure 22 as the percentile data has been skewed because of insufficient data in Q1 and Q2 (zero and 25% respectively) and the extreme readings associated with the dust storm which affected most of eastern Australia on 22 and 23 September, 2009.

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 16.7 | 0 | 33.2 | 32.4 | 32.0 | 28.1 | 22.5 | 17.9 | 14.4 |
| 2005 | 9.6 | 1 | 50.64 | 47.2 | 43.8 | 34.8 | 27.5 | 19.5 | 12.7 |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |
| 2009 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 2010 | 57.6 | 0 | 23.8 | 19.7 | 17.1 | 14.7 | 13.7 | 11.1 | 8.4 |
| 2011 | 97.0 | 0 | 29.2 | 22.3 | 20.9 | 16.9 | 14.4 | 11.0 | 7.9 |
| 2012 | 95.1 | 0 | 49.5 | 22.8 | 20.2 | 17.0 | 14.9 | 12.1 | 8.7 |
| 2013 | 92.9 | 1 | 57.8 | 26.5 | 24.4 | 19.9 | 15.8 | 12.0 | 8.6 |

Figure 23: Stati ti al summary for daily maximum 24-hour PM10 Civic 2004 – 2013

60.0

50.0

40.0

30.0

20.0

10.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

Note No PM10 monitoring was conducted at Civic in 2009.

2.5

### Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2013

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.1 | 15 | 38.3 | 35.8 | 31.5 | 23.5 | 16.6 | 9.5 | 6.2 |
| 2005 | 73.6 | 14 | 38.6 | 31.4 | 29.3 | 25.0 | 20.7 | 9.0 | 4.9 |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |
| 2010 | 95.1 | 2 | 52.4 | 22.1 | 20.9 | 17.4 | 14.3 | 7.8 | 4.4 |
| 2011 | 92.1 | 4 | 32.8 | 25.6 | 22.9 | 20.0 | 12.5 | 7.0 | 4.5 |
| 2012 | 95.1 | 3 | 29.2 | 23.8 | 19.8 | 16.5 | 13.2 | 8.3 | 5.0 |
| 2013 | 98.6 | 6 | 38.4 | 30.5 | 22.7 | 19.2 | 12.9 | 8.1 | 5.2 |

Figure 24: Stati ti al summary for daily maximum 24-hour PM2.5 Monash 2004 – 2013

30.0

25.0

20.0

15.0

10.0

5.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011	2012	2013

# Text boxes

NEPM standard

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

parts per million

NEPM standard

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

parts per million

parts per million

NEPM standard

0.14

0.12

0.1

0.08

0.06

0.04

0.02

0

parts per million

NEPM standard

0.14

0.12

0.1

0.08

0.06

0.04

0.02

0

parts per million

NEPM standard

0.120

0.100

0.080

0.060

0.040

0.020

0.000

parts per million

NEPM standard

0.12

0.1

0.08

0.06

0.04

0.02

0

NEPM standard

parts per million

NEPM standard

parts per million

PM

NEPM standard

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

NEPM standard

70.0

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

PM

NEPM advisory standard

micrograms per cubic metre

PM

3

PM

NEPM Standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

NEPM standard

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

NEPM standard

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile 75 %ile 50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM Standard

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM advisory standard

micrograms per cubic metre