ACT AIR QUALITY REPORT 2011

Environment Protection Authority | June 2012

# TABLE OF CONTENTS

LIST OF TABLES	ii

LIST OF FIGURES	iii

LIST OF DEFINITIONS AND ABBREVIATIONS	iv

OVERVIEW	1

MONITORING SUMMARY	2

Current Performance Monitoring Stations	2

Monitoring Methods	4

NATA Accreditation Status	4

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL	5

Carbon monoxide	7

Nitrogen dioxide	8

Ozone	10

PM10	12

PM2.5	14

ANALYSIS OF AIR QUALITY MONITORING	15

Carbon monoxide	15

Nitrogen dioxide	15

Ozone	16

PM10	16

PM2.5	17

ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL	18

APPENDIX A: STATISTICAL SUMMARY AND TRENDS	19

Carbon monoxide	19

Nitrogen dioxide	21

Ozone	24

PM10	28

PM2.5	30

# LIST OF TABLES

Table 1 Summary of stations’ siting compliance with AS 3580.1.1-2007	2

Table 2 Methods used for monitoring AAQ NEPM pollutants	4

Table 3: AAQ NEPM standards and goals	5

Table 4: 2011 compliance summary for CO	7

Table 5: 2011 compliance summary for NO2	8

Table 6: 2011 compliance summary for O3	10

Table 7: 2011 compliance summary for PM10	12

Table 8: 2011 compliance summary for PM2.5	14

Table 9: 2011 summary statistics for daily peak 8-hour CO	15

Table 10: 2011 summary statistics for daily peak 1-hour NO2	15

Table 11: 2011 summary statistics for daily peak 1-hour O3	16

Table 12: 2011 summary statistics for daily peak 4-hour O3	16

Table 13: 2011 summary statistics for daily peak PM10	16

Table 14: 2011 summary statistics for daily peak PM2.5	17

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2002 – 2011	19

Table 16: Statistical summary for daily maximum 8-hour CO Civic 2002 – 2011	20

Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2002 – 2011	21

Table 18: Statistical summary for daily maximum 1-hour NO2 Civic 2002 – 2011	22

Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2002 – 2011	24

Table 20: Statistical summary for daily maximum 1-hour O3 Civic 2002 – 2011	25

Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2002 – 2011	26

Table 22: Statistical summary for daily maximum 4-hour O3 Civic 2002 – 2011	27

Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2002 – 2011	28

Table 24: Statistical summary for daily maximum 24-hour PM10 Civic 2002 – 2011	29

Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2011	30

# LIST OF FIGURES

Figure 1: Daily max for CO 8-hr average - Monash	7

Figure 2: Daily max for CO 8-hr average - Civic	8

Figure 3: Daily max for NO2 - Monash	9

Figure 4: Daily max for NO2 – Civic	9

Figure 5: Daily max for 1 hour O3 – Monash	10

Figure 6: Daily max for 1 hour O3 – Civic	11

Figure 7: Daily max for 4 hours O3 - Monash	11

Figure 8: Daily max for 4 hours O3 - Civic	12

Figure 9: Daily max for PM10 – Monash	13

Figure 10: Daily max for PM10 – Civic	13

Figure 11: Daily max for PM2.5 – Monash	14

Figure 12: Statistical summary for daily maximum 8-hour CO Monash 2002 – 2011	19

Figure 13: Statistical summary for daily maximum 8-hour CO Civic 2002 – 2011	20

Figure 14: Statistical summary for daily maximum 1-hour NO2 Monash 2002 – 2011	21

Figure 15: Statistical summary for daily maximum 1-hour NO2 Civic 2002 – 2011	22

Figure 16: Annual average 1-hour NO2 Monash 2002 – 2011	23

Figure 17: Annual average 1-hour NO2 Civic 2002 – 2011	23

Figure 18: Statistical summary for daily maximum 1-hour O3 Monash 2002 – 2011	24

Figure 19: Statistical summary for daily maximum 1-hour O3 Civic 2002 – 2011	25

Figure 20: Statistical summary for daily maximum 4-hour O3 Monash 2002 – 2011	26

Figure 21: Statistical summary for daily maximum 4-hour O3 Civic 2002 – 2011	27

Figure 22: Statistical summary for daily maximum 24-hour PM10 Monash 2002 – 2011	28

Figure 23: Statistical summary for daily maximum 24-hour PM10 Civic 2002 – 2011	29

Figure 24: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2011	30

Figure 25: Annual average 24-hour PM2.5 Monash 2004 - 2011	31

# LIST OF DEFINITIONS AND ABBREVIATIONS

| Term | Definition |
| --- | --- |
| AAQ NEPM | National Environment Protection (Ambient Air Quality ) Measure |
| ACT | Australian Capital Territory |
| CO | Carbon Monoxide |
| BAM | Beta Attenuation Monitor |
| NATA | National Association of Testing Authorities |
| ND | Not Demonstrated |
| NEPC | National Environment Protection Council |
| NO2 | Nitrogen Dioxide |
| O3 | Ozone |
| PMS | Performance Monitoring Station |
| PM2.5 | Particles with an equivalent aerodynamic diameter less than or equal to 2.5 Micrometers |
| PM10 | Particles with an equivalent aerodynamic diameter less than or equal to 10 Micrometers |
| ppm | Parts per million by volume – parts of pollutant per million parts of air |
| Q | Quarter (e.g. Q1 means the first quarter of the year) |
| SO2 | Sulphur Dioxide |
| µg/m3 | micrograms per cubic metre |

# OVERVIEW

This report presents the results of ambient air quality monitoring in the ACT for the 2011 calendar year and assesses them in accordance with the requirements of the National Environment Protection (Ambient Air Quality) Measure (AAQ NEPM) which was made by the National Environment Protection Council (NEPC) on 26 June 1998.

Monitoring results demonstrate that the major impacts on Canberra’s air quality in 2011, as in previous years, came from the accumulation of combustion particles from wood heaters in cold, highly stable air, hazard reduction burns and dust storms. With the exception of particulate matter less than 2.5 microns (PM2.5) all measured parameters are below the AAQ NEPM standards.

There were four exceedances of the PM2.5 24-hr advisory reporting standard which occurred in May and July 2011. These exceedences were due to wood heater emissions in winter.

Monitoring was performed in accordance with the ACT’s monitoring plan, AAQ NEPM Technical Papers and ACT Health’s accreditation by the National Association of Testing Authorities (NATA).

# MONITORING SUMMARY

## Current Performance Monitoring Stations

The ACT Government has been undertaking ambient air quality monitoring in Canberra since the early 1990’s. The Health Directorate is responsible for the Government’s ambient air quality monitoring network. The Environment and Sustainable Development Directorate is responsible for annual reporting under the AAQ NEPM.

The AAQ NEPM monitoring network in the ACT currently consists of two performance monitoring stations (PMS) at Monash and Civic respectively. The Monash station is approximately 300 metres west of Cockcroft Avenue in the Monash district playing fields. The Civic station is located at the northern end of the carpark on the western side of the Olympic swimming pool adjacent to Allara Street. The compliance and non-compliance criteria for both PMS against the siting standard AS/NZS 3580.1.1:2007 are listed in Table 1 below.

### Table 1 Summary of stations’ siting compliance with AS 3580.1.1-2007

| Station | Station type | Height above ground | Minimum distance to support structure | Clear sky angle of 120° | Unrestricted airflow of 270°/360° | 20m from trees | No boilers or incinerators nearby | Minimum distance from road or traffic |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Monash | T |  |  |  |  |  |  |  |
| Civic | P |  |  |  |  |  |  |  |

T denotes trend; P denotes performance

Under Clause 13 of the AAQ NEPM a PMS should, to the extent practicable, be sited in accordance with AS/NZS 3580.1.1:2007 and must be located in a manner such that they contribute to obtaining a representative measure of the air quality likely to be experienced by the general population in the region. Unfortunately as can see from Table 1 the Civic station is not sited in accordance with the standard. In addition to this it is located on the outskirts of the central business district of Civic and is not representative of general population exposure as required by Clause 13(2) of the AAQ NEPM.

Based on the 2012-13 ACT Budget released on 5 June 2012, the ACT Government will allocate funding for establishing another PMS that would be fully compliant with the AAQ NEPM. The Health Directorate has consulted within Government and based on a preliminary analysis of site requirements/constraints short listed a site in the central Belconnen area.

Until this AAQ NEPM monitoring station can be established, data from the Civic station, whilst not sited or located in accordance with Clause 13 of the AAQ NEPM, is being used for annual reporting purposes.

Consistent with the ACT’s Ambient Air Quality Monitoring Plan, which was approved by NEPC in 2001, this report only covers four of the six criteria pollutants, namely carbon monoxide (CO), nitrogen dioxide (NO2), photochemical oxidants as ozone (O3) and particulate matter less than 10

micrometres (PM10).  Because of a lack of heavy industry the ACT has never monitored sulphur dioxide (SO2), and ceased monitoring lead in July 2002, following the phase out of leaded fuel on 1 January 2002, with ambient air lead levels being less than 2% of the standard. The report also covers PM2.5.

Both stations contain instrumentation that continuously monitors CO, O3, and NO2. PM10 and PM2.5 monitoring is undertaken at Monash and only PM10 monitoring at Civic.

## Monitoring Methods

The ACT monitoring is conducted in accordance with the relevant Australian standard as shown in Table 2.

### Table 2 Methods used for monitoring AAQ NEPM pollutants

| Pollutant | Standard | Title | Method Used |
| --- | --- | --- | --- |
| Carbon Monoxide | AS 3580.7.1-1992 | Ambient Air – Determination of Carbon Monoxide – Direct Reading Instrument Method | Gas filter correlation/ Infrared. |
| Nitrogen dioxide | AS 3580.5.1-1993 | Ambient Air – Determination of Oxides of Nitrogen – Chemiluminescence Method | Gas phase chemiluminescence. |
| Photochemical oxidant (ozone) | AS 3580.6.1-1990 | Ambient Air – Determination of Ozone – Direct Reading Instrument Method | Non-dispersive ultraviolet. |
| Particles PM10 | AS 3580.9.11-2008 | Method for sampling and analysis of ambient air Method 9.11: Determination of suspended particles matter – PM10 beta attenuation monitors | Beta Attenuation Monitor (BAM) |
| PM10 | AS/NZS 3580.9.6- 2003 | Methods for sampling and analysis of ambient air - Determination of suspended particulate matter - PM10 high volume sampler with size- selective inlet - Gravimetric method | Gravimetric reference method |
| PM2.5 | AS/NZS 3580.9.10- 2006 | Reference Method for the Determination of Fine Particulate matter as PM2.5 in the Atmosphere | Gravimetric reference method |

NATA Accreditation Status

The ACT Government monitoring network is accredited by NATA for the measurement of all AAQ NEPM pollutants except SO2 as required under Clause 12 of the AAQ NEPM.

# ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL

For the purpose of this report, air quality is assessed against the AAQ NEPM standards and goals as specified in Schedule 2 of the AAQ NEPM and reproduced in Table 3.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3,Table 3).

The goal of the AAQ NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specified in Schedule 2 of the AAQ NEPM. The extent is expressed as a maximum allowable number of exceedences for each standard (refer to column 4,Table 3). These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfires, which cannot be controlled through normal air quality management programs.

The AAQ NEPM also specifies advisory reporting standards for PM2.5. The goal for PM2.5 is to collect sufficient data to facilitate a review of the PM2.5 standards, which has been completed through the review of the AAQ NEPM.

### Table 3: AAQ NEPM standards and goals

| Pollutant | Averaging Period | Maximum concentration | Goal within 10 years Maximum allowable exceedences |
| --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year none |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year none |
| Lead | 1 year | 0.050 μg/m3 | none |
| Particles as PM10 | 1 day | 50 μg/m3 | 5 days a year |
| Particles as PM2. # 5 | 1 day 1 year | 25 μg/m3 8 μg/m3 | Not applicable Not applicable |

# - Advisory reporting standards only

The following tables (Table 4 to Table 8) summarise compliance with the standards and goals of the AAQ NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded, the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

A station’s performance is assessed as complying with the AAQ NEPM (i.e. ’MET’) if the number of exceedances is no more than the number specified in Schedule 2 of the AAQ NEPM and data availability was at least 75% in each quarter of the year. A region demonstrates compliance with the AAQ NEPM when either all stations in the region demonstrate compliance, or when the region meets approved pollutant screening criteria.

A station’s performance is assessed as not complying with the AAQ NEPM (i.e. ‘NOT MET’) if there is more than the number of exceedances specified in Schedule 2 of the AAQ NEPM, even if the data availability rates are less than the 75% required.

A station’s performance is assessed as ‘NOT DEMONSTRATED’ (ND) if it records exceedances on a number of days less than that allowed, but has data availability rates less than 75% in any quarter. This may be due to instrument failures, temporary closures for upgrading or closures to allow relocation of the station.

These categories (i.e. MET, NOT MET and ND) are used in the tables on the following pages.

Carbon monoxide

During 2011, no exceedences of the CO standard were recorded in the ACT and compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 4: 2011 compliance summary for CO

AAQ NEPM standard - 9.0 ppm (8-hr average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 95.6 | 94.4 | 95.6 | 95.4 | 95.3 | 0 | MET |
| Civic | 94.2 | 93.4 | 93.6 | 94.7 | 94.0 | 0 | MET |

10.0

Monash

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

### Figure 1: Daily max for CO 8-hr average - Monash

10.0

Civic

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

### Figure 2: Daily max for CO 8-hr average - Civic

Nitrogen dioxide

During 2011, no exceedences of the NO2 standards were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated at Monash but not at Civic because of instrument failures at various times throughout the third quarter.

### Table 5: 2011 compliance summary for NO2

AAQ NEPM standard – 0.12 ppm (1 hour average), 0.03 ppm (1 year average)

### er of our ences ys)

Performance against the standards and goal

Monash

### Figure 3: Daily max for NO2 - Monash

Civic

### Figure 4: Daily max for NO2 – Civic

## Ozone

During 2011, no exceedences of the 1 hour and 4 hour standards for O3 were recorded in the ACT, and compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 6: 2011 compliance summary for O3

AAQ NEPM standard – 0.10 ppm (1 hour average), 0.08 ppm (4 hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Monash | 95.7 | 93.8 | 95.6 | 95.2 | 95.1 | 0 | 0 | MET | MET |
| Civic | 93.8 | 86.1 | 95.8 | 95.8 | 92.9 | 0 | 0 | MET | MET |

Monash

### Figure 5: Daily max for 1 hour O3 – Monash

### Figure 6: Daily max for 1 hour O3 – Civic

Monash

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

### Figure 7: Daily max for 4 hours O3 - Monash

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

### Figure 8: Daily max for 4 hours O3 - Civic

PM10

During 2011, there were no exceedences of the 24-hr PM10 standard recorded in the ACT, and compliance against the AAQ NEPM goal was demonstrated at both stations.

### Table 7: 2011 compliance summary for PM10

AAQ NEPM standard 50 g/m3 1 day average

| Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 96.7 | 100 | 100 | 100 | 98.9 | 0 | MET |
| Civic | 98.9 | 100 | 100 | 91.7 | 96.7 | 0 | MET |

Monash

### Figure 9: Daily max for PM10 – Monash.

Civic

### Figure 10: Daily max for PM10 – Civic.

PM2.5

Four exceedences of the 24-hr advisory reporting standard were recorded at Monash during 2011.

### Table 8: 2011 compliance summary for PM2.5

AAQ NEPM standard – 25 g/m3 (1 day), 8 g/m3 (1year)

| Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration (g/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash | 95.6 | 98.9 | 94.6 | 85.1 | 92.3 | 6.4 | 4 |

35.0

Monash

30.0

25.0

20.0

15.0

10.0

5.0

0.0

### Figure 11: Daily max for PM2.5 – Monash.

ANALYSIS OF AIR QUALITY MONITORING

Annual summary statistics contained in Table 9 to Table 14 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The AAQ NEPM states that the short-term standards should not be exceeded on more than one day for CO, NO2 and O3, and on no more than five days per year for PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

## Carbon monoxide

### Table 9: 2011 summary statistics for daily peak 8-hour CO

AAQ NEPM standard - 9.0 ppm (8-hr average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 360 357 | 2.2 2.0 | 21 May 03:00 02 Aug 23:00 | 2.1 1.9 | 22 May 05:00 04 Aug 21:00 |

Carbon monoxide levels are well below the AAQ NEPM standard. Because of both an improvement in vehicle emissions and a decline in wood heaters numbers, levels are trending down (refer to Figure 12 and Figure 13). The highest recorded value in the ACT during 2011 was 2.2ppm at Monash. This is only 24% of the standard.

## Nitrogen dioxide

### Table 10: 2011 summary statistics for daily peak 1-hour NO2

AAQ NEPM standard 0.12 ppm (1 hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 353 324 | 0.043 0.046 | 22 Sept 21:00 22 Sept 21:00 | 0.033 0.038 | 04 Sept 20:00 20 Oct 22:00 |

Nitrogen dioxide levels are well below the AAQ NEPM standard and have remained stable over the last decade. The highest recorded 1 hour value during 2011 was 0.046ppm at Civic, which is only

38% of the standard.  The highest recorded annual average in 2011 was 0.008ppm at Civic. This is only 27% of the standard.

## Ozone

### Table 11: 2011 summary statistics for daily peak 1-hour O3

AAQ NEPM standard 0.10 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 362 352 | 0.056 0.052 | 22 Sept 15:00 20 Sept 01:00 | 0.053 0.052 | 20 Sept 01:00 22 Sept 14:00 |

### Table 12: 2011 summary statistics for daily peak 4-hour O3

AAQ NEPM standard 0.08 ppm (4-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 361 352 | 0.054 0.050 | 22 Sept 18:00 20 Sept 03:00 | 0.052 0.049 | 09 Nov 18:00 22 Sept 17:00 |

Ozone levels are below the AAQ NEPM standard. The highest recorded 1-hour value in the ACT during 2011 was 0.056ppm at Monash, which is 56% of the standard. The highest recorded 4-hour value in the ACT during 2011 was 0.054ppm at Monash. This is 68% of the standard.

PM10

### Table 13: 2011 summary statistics for daily peak PM10

AAQ NEPM standard 50 g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic | 362 354 | 40.0 29.2 | 14 Nov 20 May | 31.9 21.5 | 20 May 19 May |

PM10 levels are below the AAQ NEPM standard. The highest PM10 level recorded during 2011 was 40.0μg/m3 on 14 November 2011. This is 80% of the AAQ NEPM standard.

PM2.5

### Table 14: 2011 summary statistics for daily peak PM2.5

AAQ NEPM standard 25 g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest (g/m3) | Highest (date) | 6th Highest (g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash | 336 | 32.8 | 21 May | 23.8 | 24 Jun |

The 24-hour advisory reporting standard for PM2.5 was exceeded four times at Monash. The exceedences happened during late May to early July 2011 because of particle emissions from wood heaters during winter.

# ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL

The ACT is currently compliant with the goal specified in Schedule 2 of the AAQ NEPM.

Historical monitoring indicates that the only AAQ NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions from domestic wood heaters. In more recent years exceedences of the particulate matter standard have also been attributed to dust storms and smoke from controlled burns.

The ACT Government acknowledges that woodsmoke is a problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

It will continue to implement an integrated program to address woodsmoke. This will involve public education and enforcement activities, the licensing of firewood merchants, the implementation of the ‘Don’t Burn Tonight Campaign’ and the on-going implementation of the Wood Heater Replacement Program.

It is pleasing to note that there were no exceedences of the PM10 standard in 2011 because of wood heater emissions, although monitoring clearly shows that levels increase during the winter months (refer to Figure 9 and Figure 10 for details). Since 2002 the 95th percentile for PM10 at Monash has fallen from 42.4g/m3 to 22.8g/m3. This is a significant improvement.

The ACT will also work with the Commonwealth and other jurisdictions at a national level through the Standing Council on Environment and Water to progress actions to improve air quality, in particular national reforms to manage wood heather emissions.

# APPENDIX A: STATISTICAL SUMMARY AND TRENDS

The following section provides a basic statistical summary, using percentiles, for each station and for each standard. Percentiles for daily maximum values are presented.

## Carbon monoxide

### Table 15: Statistical summary for daily maximum 8-hour CO Monash 2002 – 2011

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 92 | 0 | 4.3 | 3.7 | 3.4 | 2.9 | 2.3 | 1.2 | 0.4 |
| 2003 | 86.8 | 0 | 3.7 | 3.0 | 2.8 | 2.5 | 2.0 | 0.8 | 0.3 |
| 2004 | 94.1 | 0 | 3.2 | 2.7 | 2.5 | 2.0 | 1.6 | 0.9 | 0.5 |
| 2005 | 99.5 | 0 | 3.2 | 2.8 | 2.5 | 2.2 | 1.7 | 1.0 | 0.4 |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2010 | 99.2 | 0 | 1.8 | 1.7 | 1.6 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2011 | 98.6 | 0 | 2.2 | 1.9 | 1.8 | 1.5 | 1.1 | 0.5 | 0.2 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 12: Statistical summary for daily maximum 8-hour CO Monash 2002 – 2011

### Table 16: Statistical summary for daily maximum 8-hour CO Civic 2002 – 2011

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 86.8 | 0 | 5.1 | 4.7 | 4.4 | 3.52 | 2.9 | 1.6 | 0.6 |
| 2003 | 95.7 | 0 | 3.5 | 2.8 | 2.6 | 2.2 | 1.8 | 1.0 | 0.6 |
| 2004 | 95.7 | 0 | 4.6 | 3.6 | 3.2 | 2.3 | 1.6 | 0.6 | 0.6 |
| 2005 | 95.6 | 0 | 3.7 | 3.4 | 3.2 | 2.6 | 1.7 | 1.1 | 0.7 |
| 2006 | 95.4 | 0 | 2.8 | 2.7 | 2.6 | 2.1 | 1.4 | 0.8 | 0.5 |
| 2007 | 93.2 | 0 | 2.8 | 2.3 | 2.0 | 1.6 | 1.3 | 0.8 | 0.5 |
| 2008 | 92.7 | 0 | 2.3 | 2.1 | 2.0 | 1.6 | 1.2 | 0.7 | 0.4 |
| 2009 | 95.1 | 0 | 1.9 | 1.6 | 1.2 | 1.0 | 0.8 | 0.6 | 0.4 |
| 2010 | 98.6 | 0 | 2.0 | 1.9 | 1.8 | 1.4 | 1.2 | 0.9 | 0.6 |
| 2011 | 97.8 | 0 | 2.0 | 1.8 | 1.6 | 1.4 | 1.0 | 0.7 | 0.5 |

10.0

9.0

8.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 13: Statistical summary for daily maximum 8-hour CO Civic 2002 – 2011

Nitrogen dioxide

Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 88.3 | 0 | 0.045 | 0.036 | 0.034 | 0.031 | 0.026 | 0.022 | 0.017 |
| 2003 | 90.4 | 0 | 0.064 | 0.042 | 0.033 | 0.028 | 0.025 | 0.021 | 0.016 |
| 2004 | 91.8 | 0 | 0.040 | 0.033 | 0.031 | 0.028 | 0.026 | 0.022 | 0.018 |
| 2005 | 97.8 | 0 | 0.041 | 0.034 | 0.031 | 0.028 | 0.027 | 0.024 | 0.018 |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |
| 2010 | 89.1 | 0 | 0.037 | 0.029 | 0.028 | 0.025 | 0.023 | 0.021 | 0.017 |
| 2011 | 96.7 | 0 | 0.043 | 0.031 | 0.030 | 0.029 | 0.026 | 0.022 | 0.015 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 14: Statistical summary for daily maximum 1-hour NO2 Monash 2002 – 2011

Table 18: Statistical summary for daily maximum 1-hour NO2 Civic 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 88.2 | 0 | 0.062 | 0.050 | 0.044 | 0.038 | 0.034 | 0.029 | 0.024 |
| 2003 | 83.6 | 0 | 0.087 | 0.050 | 0.045 | 0.034 | 0.028 | 0.022 | 0.018 |
| 2004 | 88.3 | 0 | 0.042 | 0.037 | 0.035 | 0.030 | 0.027 | 0.022 | 0.018 |
| 2005 | 95.3 | 0 | 0.040 | 0.036 | 0.033 | 0.030 | 0.029 | 0.024 | 0.020 |
| 2006 | 95.2 | 0 | 0.044 | 0.035 | 0.034 | 0.031 | 0.028 | 0.022 | 0.018 |
| 2007 | 92.8 | 0 | 0.059 | 0.042 | 0.039 | 0.035 | 0.030 | 0.025 | 0.021 |
| 2008 | 88.6 | 0 | 0.046 | 0.037 | 0.035 | 0.033 | 0.030 | 0.026 | 0.020 |
| 2009 | 79.5 | 0 | 0.044 | 0.038 | 0.036 | 0.030 | 0.027 | 0.023 | 0.018 |
| 2010 | 74.9 | 0 | 0.039 | 0.035 | 0.033 | 0.030 | 0.027 | 0.024 | 0.021 |
| 2011 | 88.8 | 0 | 0.046 | 0.036 | 0.035 | 0.032 | 0.029 | 0.023 | 0.018 |

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 15: Statistical summary for daily maximum 1-hour NO2 Civic 2002 – 2011

0.035

0.025

0.020

0.015

0.010

0.005

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 16: Annual average 1-hour NO2 Monash 2002 – 2011

0.035

0.030

0.025

0.020

0.015

0.010

0.005

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 17: Annual average 1-hour NO2 Civic 2002 – 2011

Ozone

Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 93.5 | 0 | 0.063 | 0.055 | 0.052 | 0.047 | 0.042 | 0.032 | 0.024 |
| 2003 | 92.4 | 0 | 0.102 | 0.069 | 0.061 | 0.050 | 0.045 | 0.035 | 0.025 |
| 2004 | 94.1 | 0 | 0.064 | 0.56 | 0.054 | 0.048 | 0.044 | 0.038 | 0.030 |
| 2005 | 97.8 | 0 | 0.065 | 0.058 | 0.053 | 0.045 | 0.041 | 0.034 | 0.030 |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |
| 2010 | 86.6 | 0 | 0.051 | 0.048 | 0.046 | 0.042 | 0.037 | 0.033 | 0.030 |
| 2011 | 99.2 | 0 | 0.056 | 0.052 | 0.047 | 0.044 | 0.040 | 0.033 | 0.028 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 18: Statistical summary for daily maximum 1-hour O3 Monash 2002 – 2011

Table 20: Statistical summary for daily maximum 1-hour O3 Civic 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 79.8 | 0 | 0.082 | 0.060 | 0.053 | 0.049 | 0.044 | 0.035 | 0.029 |
| 2003 | 93.6 | 0 | 0.094 | 0.065 | 0.055 | 0.049 | 0.045 | 0.037 | 0.031 |
| 2004 | 93.5 | 0 | 0.071 | 0.055 | 0.053 | 0.045 | 0.041 | 0.034 | 0.028 |
| 2005 | 85.5 | 0 | 0.070 | 0.061 | 0.051 | 0.042 | 0.038 | 0.032 | 0.028 |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |
| 2010 | 99.2 | 0 | 0.058 | 0.050 | 0.048 | 0.040 | 0.036 | 0.029 | 0.025 |
| 2011 | 96.4 | 0 | 0.052 | 0.046 | 0.045 | 0.041 | 0.036 | 0.030 | 0.026 |

0.120

0.100

0.080

0.060

0.040

0.020

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 19: Statistical summary for daily maximum 1-hour O3 Civic 2002 – 2011

Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 93.5 | 0 | 0.058 | 0.051 | 0.049 | 0.044 | 0.039 | 0.031 | 0.023 |
| 2003 | 92.4 | 1 | 0.082 | 0.063 | 0.058 | 0.048 | 0.043 | 0.033 | 0.025 |
| 2004 | 94.1 | 0 | 0.060 | 0.053 | 0.051 | 0.045 | 0.042 | 0.036 | 0.029 |
| 2005 | 97.5 | 0 | 0.062 | 0.054 | 0.049 | 0.044 | 0.039 | 0.033 | 0.029 |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |
| 2010 | 86.6 | 0 | 0.049 | 0.046 | 0.043 | 0.040 | 0.037 | 0.032 | 0.029 |
| 2011 | 98.9 | 0 | 0.054 | 0.048 | 0.044 | 0.041 | 0.038 | 0.032 | 0.027 |

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 20: Statistical summary for daily maximum 4-hour O3 Monash 2002 – 2011

Table 22: Statistical summary for daily maximum 4-hour O3 Civic 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 79.8 | 0 | 0.073 | 0.057 | 0.051 | 0.046 | 0.042 | 0.033 | 0.027 |
| 2003 | 93.6 | 0 | 0.078 | 0.055 | 0.051 | 0.046 | 0.042 | 0.036 | 0.029 |
| 2004 | 93.5 | 0 | 0.062 | 0.052 | 0.048 | 0.043 | 0.039 | 0.32 | 0.026 |
| 2005 | 85.5 | 0 | 0.061 | 0.054 | 0.047 | 0.040 | 0.036 | 0.031 | 0.026 |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |
| 2010 | 99.2 | 0 | 0.056 | 0.047 | 0.044 | 0.037 | 0.034 | 0.028 | 0.024 |
| 2011 | 96.4 | 0 | 0.050 | 0.044 | 0.041 | 0.038 | 0.035 | 0.029 | 0.025 |

0.090

0.080

0.070

0.060

0.050

0.040

0.030

0.020

0.010

0.000

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 21: Statistical summary for daily maximum 4-hour O3 Civic 2002 – 2011

PM10

### Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 75 | 0 | 108.4 | 56.6 | 48.5 | 42.4 | 37.7 | 25.3 | 16.2 |
| 2003 | 97.5 | 13 | 350.4 | 136.4 | 105.3 | 39.6 | 30.3 | 21.2 | 14.6 |
| 2004 | 99.7 | 3 | 52.0 | 48.2 | 46.0 | 33.8 | 28.5 | 20.7 | 14.7 |
| 2005 | 97.5 | 10 | 98.8 | 57.6 | 52.7 | 37.3 | 31.0 | 21.2 | 14.5 |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |
| 2010 | 95.4 | 0 | 48.4 | 35.6 | 27.4 | 23.5 | 20.2 | 14.7 | 10.0 |
| 2011 | 99.2 | 0 | 40.0 | 33.7 | 30.3 | 22.8 | 18.6 | 13.2 | 8.7 |

60.0

50.0

40.0

30.0

20.0

10.0

0.0

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 22: Statistical summary for daily maximum 24-hour PM10 Monash 2002 – 2011

Note 2009 data has not been included in Figure 22 as the percentile data has been skewed because of insufficient data in Q1 and Q2 (zero and twenty five percent respectively) and the extreme readings associated with the dust storm which affected most of eastern Australia on 22 and 23 September, 2009.

### Table 24: Statistical summary for daily maximum 24-hour PM10 Civic 2002 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2002 | 15.6 | 3 | 67.4 | 67.1 | 66.3 | 42.7 | 25.4 | 18.7 | 15.3 |
| 2003 | 12.6 | 0 | 20.8 | 20.8 | 20.7 | 19.3 | 17.3 | 13.6 | 9.3 |
| 2004 | 16.7 | 0 | 33.2 | 32.4 | 32.0 | 28.1 | 22.5 | 17.9 | 14.4 |
| 2005 | 9.6 | 1 | 50.64 | 47.2 | 43.8 | 34.8 | 27.5 | 19.5 | 12.7 |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |
| 2009 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 2010 | 57.6 | 0 | 23.8 | 19.7 | 17.1 | 14.7 | 13.7 | 11.1 | 8.4 |
| 2011 | 97.0 | 0 | 29.2 | 22.3 | 20.9 | 16.9 | 14.4 | 11.0 | 7.9 |

60.0

50.0

40.0

30.0

20.0

10.0

0.0

2002	2003	2004	2005	2006	2007	2008	2009	2010	2011

### Figure 23: Statistical summary for daily maximum 24-hour PM10 Civic 2002 – 2011

Note No PM10 monitoring was conducted at Civic in 2009.

PM2.5

### Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2011

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2004 | 93.1 | 15 | 38.3 | 35.8 | 31.5 | 23.5 | 16.6 | 9.5 | 6.2 |
| 2005 | 73.6 | 14 | 38.6 | 31.4 | 29.3 | 25.0 | 20.7 | 9.0 | 4.9 |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |
| 2010 | 95.1 | 2 | 52.4 | 22.1 | 20.9 | 17.4 | 14.3 | 7.8 | 4.4 |
| 2011 | 92.1 | 4 | 32.8 | 25.6 | 22.9 | 20.0 | 12.5 | 7.0 | 4.5 |

30.0

25.0

20.0

15.0

10.0

5.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011

### Figure 24: Statistical summary for daily maximum 24-hour PM2.5 Monash 2004 – 2011

10.0

9.0

7.0

6.0

5.0

4.0

3.0

2.0

1.0

0.0

2004	2005	2006	2007	2008	2009	2010	2011

### Figure 25: Annual average 24-hour PM2.5 Monash 2004 - 2011

# Text boxes

NEPM standard

parts per million

NEPM standard

parts per million

| Performance monitoring station | Numb Data availability rates Annual mean 1 h (% of hours) Concentration exceed (ppm) (da |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | 1 hour | 1 year |
|  | Q1 | Q2 Q3 Q4 Annual |  |  |  |  |  |  |
| Monash Civic | 95.5 94.1 | 94.4 94.7 89.6 93.6 89.1 70.9 90.5 86.1 | 0.0 | 05 0 0.008 0 |  |  | MET ND | MET ND |

part per million

NEPM standard

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

part per million

NEPM standard

0.140

0.120

0.100

0.080

0.060

0.040

0.020

0.000

part per million

NEPM standard

0.120

0.100

0.080

0.060

0.040

0.020

0.000

NEPM standard

part per million

0.120

0.100

0.080

0.060

0.040

0.020

0.000

NEPM standard

parts per million

NEPM standard

parts per million

NEPM standard

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

NEPM standard

60.0

50.0

40.0

30.0

20.0

10.0

0.0

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre

NEPM Standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

| NEPM standard |
| --- |
|  | 95 %ile 75 %ile 50 %ile |  |

parts per million

NEPM standard

parts per million

NEPM standard

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

parts per million

NEPM standard

95 %ile 75 %ile 50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

NEPM standard

95 %ile

75 %ile

50 %ile

parts per million

95 %ile

75 %ile

50 %ile

NEPM standard

micrograms per cubic metre

NEPM Standard

95 %ile

75 %ile

50 %ile

micrograms per cubic metre

95 %ile

75 %ile

50 %ile

NEPM advisory standard

micrograms per cubic metre

NEPM advisory standard

micrograms per cubic metre