ACT AIR QUALITY REPORT 2014

Environment Protection Authority | June 2015

# TABLE OF CONTENTS

LIST OF TABLES	ii

LIST OF FIGURES	iii

LIST OF DEFINITIONS AND ABBREVIATIONS	iv

OVERVIEW	1

MONITORING SUMMARY	2

Current Performance Monitoring Stations	2

Monitoring Methods	3

NATA Accreditation Status	3

ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL	4

Carbon monoxide	6

Nitrogen dioxide	7

Ozone	9

PM10	12

PM2.5	14

ANALYSIS OF AIR QUALITY MONITORING	16

Carbon monoxide	16

Nitrogen dioxide	16

Ozone	17

PM10	17

PM2.5	18

ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL	19

APPENDIX A: STATISTICAL SUMMARY AND TRENDS	20

Carbon monoxide	20

Nitrogen dioxide	21

Ozone	22

PM10	26

PM2.5	28

# LIST OF TABLES

Table 1 Summary of stations’ siting compliance with AS 3580.1.1:2007	2

Table 2 Methods used for monitoring AAQ NEPM pollutants	3

Table 3: AAQ NEPM standards and goals	4

Table 4: 2014 compliance summary for CO	6

Table 5: 2014 compliance summary for NO2	7

Table 6: 2014 compliance summary for O3	9

Table 7: 2014 compliance summary for PM10	12

Table 8: 2014 compliance summary for PM2.5	14

Table 9: 2014 summary statistics for daily peak 8-hour CO	16

Table 10: 2014 summary statistics for daily peak 1-hour NO2	16

Table 11: 2014 summary statistics for daily peak 1-hour O3	17

Table 12: 2014 summary statistics for daily peak 4-hour O3	17

Table 13: 2014 summary statistics for daily peak PM10	17

Table 14: 2014 summary statistics for daily peak PM2.5	18

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2005 – 2014	20

Table 17: Statistical summary for daily maximum 1-hour NO2 Monash 2005 – 2014	21

Table 19: Statistical summary for daily maximum 1-hour O3 Monash 2005 – 2014	22

Table 20: Statistical summary for daily maximum 1-hour O3 Civic 2005 – 2014	23

Table 21: Statistical summary for daily maximum 4-hour O3 Monash 2005 – 2014	24

Table 22: Statistical summary for daily maximum 4-hour O3 Civic 2005 – 2014	25

Table 23: Statistical summary for daily maximum 24-hour PM10 Monash 2005 – 2014	26

Table 24: Statistical summary for daily maximum 24-hour PM10 Civic 2005 – 2014	27

Table 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2005 – 2014	28

# LIST OF FIGURES

Figure 1: Daily max for CO 8-hour average – Monash	6

Figure 2: Daily max for CO 8-hour average – Florey	7

Figure 3: Daily max for NO2 – Monash	8

Figure 4: Daily max for NO2 – Florey	8

Figure 5: Daily max for 1 hour O3 – Monash	9

Figure 6: Daily max for 1 hour O3 – Civic	10

Figure 7: Daily max for 1 hour O3 – Florey	10

Figure 8: Daily max for 4 hours O3 - Monash	11

Figure 9: Daily max for 4 hours O3 – Civic	11

Figure 10: Daily max for 4 hours O3 – Florey	12

Figure 11: Daily max for PM10 – Monash	13

Figure 12: Daily max for PM10 – Civic	13

Figure 13: Daily max for PM10 – Florey	14

Figure 14: Daily max for PM2.5 – Monash	15

Figure 15: Daily max for PM2.5 – Florey	15

Figure 16: Statistical summary for daily maximum 8-hour CO Monash 2005 – 2014	20

Figure 17: Statistical summary for daily maximum 1-hour NO2 Monash 2005 – 2014	21

Figure 18: Annual average 1-hour NO2 Monash 2005 – 2014	22

Figure 19: Statistical summary for daily maximum 1-hour O3 Monash 2005 – 2014	23

Figure 20: Statistical summary for daily maximum 1-hour O3 Civic 2005 – 2014	24

Figure 21: Statistical summary for daily maximum 4-hour O3 Monash 2005 – 2014	25

Figure 22: Statistical summary for daily maximum 4-hour O3 Civic 2005 – 2014	26

Figure 23: Statistical summary for daily maximum 24-hour PM10 Monash 2005 – 2014	27

Figure 24: Statistical summary for daily maximum 24-hour PM10 Civic 2005 – 2014	28

Figure 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2005 – 2014	29

Figure 26: Annual average 24-hour PM2.5 Monash 2005 - 2014	29

# LIST OF DEFINITIONS AND ABBREVIATIONS

| Term | Definition |
| --- | --- |
| AAQ NEPM | National Environment Protection (Ambient Air Quality ) Measure |
| ACT | Australian Capital Territory |
| CO | Carbon Monoxide |
| BAM | Beta Attenuation Monitor |
| NATA | National Association of Testing Authorities |
| ND | Not Demonstrated |
| NO2 | Nitrogen Dioxide |
| O3 | Ozone |
| PMS | Performance Monitoring Station |
| PM2.5 | Particles with an equivalent aerodynamic diameter less than or equal to 2.5 Micrometers |
| PM10 | Particles with an equivalent aerodynamic diameter less than or equal to 10 Micrometers |
| ppm | Parts per million by volume – parts of pollutant per million parts of air |
| Q | Quarter (e.g. Q1 means the first quarter of the year) |
| SO2 | Sulfur Dioxide |
| µg/m3 | micrograms per cubic metre |

# OVERVIEW

This report presents the results of ambient air quality monitoring in the ACT for the 2014 calendar year and assesses them in accordance with the requirements of the National Environment Protection (Ambient Air Quality) Measure (AAQ NEPM) which was made by the National Environment Protection Council on 26 June 1998.

The AAQ NEPM establishes:

- requirements for monitoring air quality;

- air quality standards that are levels of specified pollutants against which air quality can be assessed; and

- a goal that the air quality standards be met to the extent specified in the NEPM. Recognising that certain events can impact on air quality, the NEPM specifies a maximum number of days on which it is permissible to exceed the standard.

The ACT monitors four of the six NEPM pollutants, namely carbon monoxide (CO), nitrogen dioxide (NO2), photochemical oxidants as ozone (O3) and particulate matter (particles less than 10 microns in diameter – PM10 and particles less than 2.5 microns in diameter – PM2.5).  Due to a lack of heavy industry, the ACT has never monitored sulfur dioxide (SO2) as it is primarily an industrial pollutant, and lead monitoring ceased in 2002 with the phase out of leaded petrol. Monitoring was performed in accordance with the ACT’s monitoring plan, AAQ NEPM Technical Papers and ACT Health’s accreditation by the National Association of Testing Authorities (NATA).

This is the first year that the ACT’s Air Quality Report includes the data from the new monitoring station located in Florey.

Monitoring results demonstrate that Canberra’s air quality is excellent compared to other capital cities, with no exceedences of the AAQ NEPM standards for CO, NO2, O3, and PM10.  The major impacts on Canberra’s air quality in 2014 came from the accumulation of combustion particles from hazard reduction burns.

There were four exceedences of the PM2.5 24-hour advisory reporting standard measured at Monash. Three exceedences occurred on 4, 10 and 23 February 2014 respectively due to smoke coming from a number of hazard reduction burns in NSW. The other exceedence happened on          3 August 2014 due to domestic wood heater emissions.

# MONITORING SUMMARY

## Current Performance Monitoring Stations

The ACT Government has been undertaking ambient air quality monitoring in Canberra since the early 1990’s. The Health Directorate is responsible for the Government’s ambient air quality monitoring network. The Environment Protection Authority within the Chief Minister, Treasury and Economic Development Directorate is responsible for annual reporting under the AAQ NEPM.

The AAQ NEPM monitoring network in the ACT currently consists of three monitoring stations at Monash, Civic and Florey respectively. The Monash station is approximately 300 metres west of Cockcroft Avenue in the Monash district playing fields. The Civic station is located at the northern end of the carpark on the western side of the Olympic swimming pool adjacent to Allara Street. The Florey station, which has been operational since 28 February 2014, is located at the end of Neumann Place, Florey in public land. The compliance and non-compliance criteria for the above stations against the siting standard AS/NZS 3580.1.1:2007 are listed in Table 1 below.

Table 1 Summary of stations’ siting compliance with AS 3580.1.1:2007

| Station | Height above ground | Minimum distance to support structure | Clear sky angle of 120° | Unrestricted airflow of 270°/360° | 20m from trees | No boilers or incinerators nearby | Minimum distance from road or traffic |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Monash | ( | ( | ( | ( | ( | ( | ( |
| Civic | ( | ( | ( | ( | ( | ( | ( |
| Florey | ( | ( | ( | ( | ( | ( | ( |

Both Monash and Florey stations contain instrumentation that continuously monitors CO, O3, NO2, PM10, and PM2.5.  Following the establishment of the Florey station, the Civic station now only monitors O3 and PM10.

## Monitoring Methods

The ACT monitoring is conducted in accordance with the relevant Australian standards as shown in Table 2. Data not meeting the requirements of these Standards are identified as invalid and not included in this report.

Table 2 Methods used for monitoring AAQ NEPM pollutants

| Pollutant | Standard | Title | Method Used |
| --- | --- | --- | --- |
| Carbon Monoxide | AS 3580.7.1-2011 | Ambient Air – Determination of Carbon Monoxide – Direct Reading Instrument Method | Gas filter correlation/ Infrared. |
| Nitrogen dioxide | AS 3580.5.1-2011 | Ambient Air – Determination of Oxides of Nitrogen – Chemiluminescence Method | Gas phase chemiluminescence. |
| Photochemical oxidant (ozone) | AS 3580.6.1-2011 | Ambient Air – Determination of Ozone – Direct Reading Instrument Method | Non-dispersive ultraviolet. |
| Particles PM10 | AS 3580.9.11-2008 | Method for sampling and analysis of ambient air Method – Determination of suspended particles matter – PM10 beta attenuation monitors | Beta Attenuation Monitor (BAM) |
| PM10 | AS/NZS 3580.9.6-2005 | Methods for sampling and analysis of ambient air - Determination of suspended particulate matter - PM10 high volume sampler with size-selective inlet - Gravimetric method | Gravimetric reference method |
| PM2.5 | AS/NZS 3580.9.10-2006 | Reference Method for the Determination of Fine Particulate matter as PM2.5 in the Atmosphere | Gravimetric reference method |

## NATA Accreditation Status

The ACT Government monitoring network is accredited by NATA for the measurement of all AAQ NEPM pollutants except SO2 as required under Clause 12 of the AAQ NEPM.

# ASSESSMENT OF COMPLIANCE WITH STANDARDS AND 2008 GOAL

For the purpose of this report, air quality is assessed against the AAQ NEPM standards and goals as specified in Schedule 2 of the AAQ NEPM and reproduced in Table 3.

The standards against which air quality is assessed are concentrations in parts per million (ppm) or micrograms per cubic metre (µg/m3) (refer to column 3, Table 3).

The goal of the AAQ NEPM is to achieve the Standards as assessed in accordance with the monitoring protocol within 10 years of commencement (i.e. 2008) to the extent specified in Schedule 2 of the AAQ NEPM.  The extent is expressed as a maximum allowable number of exceedences for each standard (shown in column 4, Table 3). These are set to account for unusual meteorological conditions and, in the case of particles, natural events such as dust storms and bushfires, which cannot be controlled through normal air quality management programs.

The AAQ NEPM also specifies advisory reporting standards for PM2.5. The goal for PM2.5 is to collect sufficient data to facilitate a review of the PM2.5 standards, which has been completed through the review of the AAQ NEPM.

Table 3: AAQ NEPM standards and goals

| Pollutant | Averaging Period | Maximum concentration | Goal within 10 years Maximum allowable exceedences | Monitoring Station |
| --- | --- | --- | --- | --- |
| Carbon monoxide | 8 hours | 9.0 ppm | 1 day a year | Monash Florey |
| Nitrogen dioxide | 1 hour 1 year | 0.12 ppm 0.03 ppm | 1 day a year none | Monash Florey |
| Photochemical oxidants | 1 hour 4 hours | 0.10 ppm 0.08 ppm | 1 day a year 1 day a year | Monash Florey Civic |
| Sulfur dioxide | 1 hour 1 day 1 year | 0.20 ppm 0.08 ppm 0.02 ppm | 1 day a year 1 day a year none | Not monitored |
| Lead | 1 year | 0.050 μg/m3 | none | Not monitored |
| Particles as PM10 | 1 day | 50 μg/m3 | 5 days a year | Monash Florey Civic |
| Particles as PM2.5 | 1 day 1 year | 25 μg/m3 8 μg/m3 | Not applicable Not applicable | Monash Florey |

The following tables (Table 4 to Table 8) summarise compliance with the standards and goals of the AAQ NEPM. For each pollutant, the data availability (quarterly and annual), the number of days when standards were exceeded, the annual mean (where an annual standard exists) and an assessment of compliance, are given for each monitoring station.

Air quality is assessed as complying with the AAQ NEPM (i.e. ’MET’) if the number of exceedences is no more than the number specified in Schedule 2 of the AAQ NEPM and data availability was at least 75% in each quarter of the year.

Air quality is assessed as not complying with the AAQ NEPM (i.e. ‘NOT MET’) if there is more than the number of exceedences specified in Schedule 2 of the AAQ NEPM.

Air quality is assessed as ‘NOT DEMONSTRATED’ (ND) if there has been insufficient data collected to demonstrate that the standards and goal have been met or not met.

During 2014, compliance was not demonstrated at Florey as this station was only fully operational from 28 February 2014 onwards and did not meet the 75% minimum data availability requirement in the first quarter.

These categories (i.e. MET, NOT MET and ND) are used in the tables on the following pages.

## Carbon monoxide

During 2014, no exceedences of the CO standard were recorded in the ACT and compliance against the AAQ NEPM goal was demonstrated at Monash.

Table 4: 2014 compliance summary for CO

AAQ NEPM standard - 9.0 ppm (8-hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash Florey | 94.7 36.6 | 94.9 89.0 | 93.7 95.4 | 92.7 95.1 | 94.0 79.2 | 0 0 | MET ND |

Figure 1: Daily max for CO 8-hour average – Monash

Figure 2: Daily max for CO 8-hour average – Florey

## Nitrogen dioxide

During 2014, no exceedences of the NO2 standards were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated at Monash.

Table 5: 2014 compliance summary for NO2

AAQ NEPM standard – 0.12 ppm (1-hour average), 0.03 ppm (1-year average)

| Performance monitoring station | Data availability rates (% of hours) | Annual mean Concentration (ppm) | Number of 1 hour exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 hour | 1 year |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |  |  |
| Monash Florey | 91.4 33.4 | 94.9 89.0 | 95.7 95.4 | 94.5 94.5 | 94.1 78.3 | 0.005 0.006 | 0 0 | MET ND | MET ND |

Figure 3: Daily max for NO2 – Monash

Figure 4: Daily max for NO2 – Florey

## Ozone

During 2014, no exceedences of the 1-hour and 4-hour standards for O3 were recorded in the ACT, and compliance against the AAQ NEPM goal was demonstrated at Monash and Civic.

Table 6: 2014 compliance summary for O3

AAQ NEPM standard – 0.10 ppm (1-hour average), 0.08 ppm (4-hour average)

| Performance monitoring station | Data availability rates (% of hours) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual | 1 hour | 4 hours | 1 hour | 4 hours |
| Monash Civic Florey | 94.8 91.6 36.5 | 95.8 95.7 89.0 | 95.7 95.5 95.6 | 92.9 93.1 95.7 | 94.8 94.0 79.4 | 0 0 0 | 0 0 0 | MET MET ND | MET MET ND |

Figure 5: Daily max for 1 hour O3 – Monash

Figure 6: Daily max for 1 hour O3 – Civic

Figure 7: Daily max for 1 hour O3 – Florey

Figure 8: Daily max for 4 hours O3 - Monash

Figure 9: Daily max for 4 hours O3 – Civic

Figure 10: Daily max for 4 hours O3 – Florey

## PM10

During 2014, no exceedences of the 24-hour PM10 standard were recorded in the ACT. Compliance against the AAQ NEPM goal was demonstrated at Monash and Civic.

Table 7: 2014 compliance summary for PM10

AAQ NEPM standard 50 (g/m3 1-day average

| Performance monitoring station | Data availability rates (% of days) | Number of exceedences (days) | Performance against the standards and goal |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash Civic Florey | 100 97.8 46.7 | 100 95.6 89.0 | 100 94.6 97.8 | 91.3 92.4 98.9 | 97.8 95.1 83.3 | 0 0 0 | MET MET ND |

Figure 11: Daily max for PM10 – Monash

Figure 12: Daily max for PM10 – Civic

Figure 13: Daily max for PM10 – Florey

## PM2.5

Four exceedences of the 24-hour advisory reporting standard were recorded at Monash during 2014.

Table 8: 2014 compliance summary for PM2.5

AAQ NEPM standard – 25 (g/m3 (1-day), 8 (g/m3 (1-year)

| Performance monitoring station | Data availability rates (% of days) | Annual mean Concentration ((g/m3) | Number of exceedences (days) |
| --- | --- | --- | --- |
|  | Q1 | Q2 | Q3 | Q4 | Annual |  |  |
| Monash Florey | 97.8 43.3 | 73..6 79.1 | 82.6 85.9 | 96.7 88.0 | 87.7 74.2 | 7.1 5.9 | 4 0 |

Figure 14: Daily max for PM2.5 – Monash

Figure 15: Daily max for PM2.5 – Florey

# ANALYSIS OF AIR QUALITY MONITORING

Annual summary statistics contained in Table 9 to Table 14 below allow assessment of air quality against the standards and the extent of compliance with the goal. Instances where the standard or goal has been exceeded are highlighted in bold. The AAQ NEPM states that the short-term standards should not be exceeded on more than one day for CO, NO2 and O3, and on no more than five days per year for PM10. The second highest daily value for the year (or the sixth for PM10) indicates the extent to which the standards are or are not met.

## Carbon monoxide

Table 9: 2014 summary statistics for daily peak 8-hour CO

AAQ NEPM standard - 9.0 ppm (8-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 365 309 | 1.8 2.2 | 04 Jul 03:00 26 May 20:00 | 1.7 1.7 | 09 Aug 06:00 22 Jun 05:00 |

Carbon monoxide levels are well below the AAQ NEPM standard. The highest recorded value in the ACT during 2014 was 2.2ppm at Florey, which is 24% of the standard.

## Nitrogen dioxide

Table 10: 2014 summary statistics for daily peak 1-hour NO2

AAQ NEPM standard 0.12 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 365 309 | 0.036 0.045 | 20 Nov 21:00 26 May 13:00 | 0.032 0.035 | 13 Nov 21:00 13 Nov 21:00 |

Nitrogen dioxide levels are well below the AAQ NEPM standard and have remained stable over the last decade. The highest recorded 1-hour value during 2014 was 0.045ppm at Florey, which is only 38% of the standard.  The highest recorded annual average in 2014 was 0.006ppm at Florey (refer to table 5). This is 20% of the annual standard 0.03ppm.

## Ozone

Table 11: 2014 summary statistics for daily peak 1-hour O3

AAQ NEPM standard 0.10 ppm (1-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 365 365 309 | 0.087 0.060 0.074 | 18 Feb 22:00 08 Feb 11:00 05 May 13:00 | 0.065 0.055 0.041 | 31 Jan 10:00 22 Jun 00:00 07 Nov 14:00 |

Table 12: 2014 summary statistics for daily peak 4-hour O3

AAQ NEPM standard 0.08 ppm (4-hour average)

| Performance monitoring station | Number of valid days | Highest (ppm) | Highest (date/time) | 2nd Highest (ppm) | 2nd Highest (date/time) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 365 365 309 | 0.060 0.047 0.040 | 02 Feb 17:00 18 Jan 18:00 07 Nov 16:00 | 0.060 0.047 0.038 | 18 Jan 12:00 08 Feb 13:00 05 May 10:00 |

Ozone levels are below the AAQ NEPM standard. The highest recorded 1-hour value in the ACT during 2014 was 0.087ppm at Monash, which is 87% of the standard. The highest recorded 4-hour value in the ACT during 2014 was 0.060ppm at Monash, which is 75% of the standard.

## PM10

Table 13: 2014 summary statistics for daily peak PM10

AAQ NEPM standard 50 (g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest ((g/m3) | Highest (date) | 6th Highest ((g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Civic Florey | 347 357 304 | 39.3 31.4 30.2 | 10 February 17 December 17 December | 24.6 22.6 24.4 | 15 May 04 February 24 February |

PM10 levels are below the AAQ NEPM standard. The highest PM10 level recorded during 2014 was 39.3μg/m3 at Monash on 10 February 2014.

## PM2.5

Table 14: 2014 summary statistics for daily peak PM2.5

AAQ NEPM standard 25 (g/m3 (24-hour average)

| Performance monitoring station | Number of valid days | Highest ((g/m3) | Highest (date) | 6th Highest ((g/m3) | 6th Highest (date) |
| --- | --- | --- | --- | --- | --- |
| Monash Florey | 360 271 | 31.5 22.8 | 04 February 22 June | 21.9 17.5 | 24 February 09 August |

The 24-hour advisory reporting standard for PM2.5 was exceeded four times at Monash. Three exceedences occurred on 4, 10 and 23 February 2014 respectively due to smoke coming from a number of hazard reduction burns in NSW. The other exceedence happened on 3 August 2014 due to domestic wood heater emissions.

# ASSESSMENT OF PROGRESS TOWARDS ACHIEVING THE GOAL

The ACT is currently compliant with the goal specified in Schedule 2 of the AAQ NEPM.

Historical monitoring results indicate that the only AAQ NEPM pollutant of concern in the Canberra airshed is particulate matter, which increases during winter because of emissions from domestic wood heaters.  In more recent years exceedences of the particulate matter standards have also been attributed to dust storms and smoke from controlled burns.

The ACT Government acknowledges that woodsmoke is a problem and is working towards addressing the issue in an informed and measured manner to ensure a satisfactory outcome for all Canberrans.

It will continue to implement an integrated program to address woodsmoke. This will involve public education and enforcement activities, the licensing of firewood merchants, the implementation of the ‘Don’t Burn Tonight Campaign’ and ‘Burn Right Tonight Campaign’, and the on-going administration of the Wood Heater Replacement Program.

The ACT is also working with the Commonwealth and other jurisdictions at a national level to progress actions to improve air quality. At the Environment Ministers Meeting on 29 April 2014, Ministers signalled their intention to vary the AAQ NEPM for particles reflecting the latest scientific understanding on health risks arising from particle pollution. The Measure seeks to establish a more stringent reporting standard for particle pollution (PM2.5 and PM10).

# APPENDIX A: STATISTICAL SUMMARY AND TRENDS

The following section provides a basic statistical summary, using percentiles, for Monash and Civic stations and for each standard. Percentiles for daily maximum values are presented. As the Florey station is newly-established, there is insufficient data to show the statistical summary and trends.

## Carbon monoxide

Table 15: Statistical summary for daily maximum 8-hour CO Monash 2005 – 2014

| Year | Data Availability (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 99.5 | 0 | 3.2 | 2.8 | 2.5 | 2.2 | 1.7 | 1.0 | 0.4 |
| 2006 | 99.7 | 0 | 3.7 | 2.8 | 2.6 | 2.2 | 1.8 | 1.1 | 0.4 |
| 2007 | 95.3 | 0 | 2.6 | 2.5 | 2.4 | 2.0 | 1.5 | 0.7 | 0.4 |
| 2008 | 88.0 | 0 | 2.4 | 2.2 | 2.1 | 1.8 | 1.5 | 0.8 | 0.3 |
| 2009 | 96.4 | 0 | 2.0 | 1.7 | 1.5 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2010 | 99.2 | 0 | 1.8 | 1.7 | 1.6 | 1.4 | 1.1 | 0.6 | 0.3 |
| 2011 | 98.6 | 0 | 2.2 | 1.9 | 1.8 | 1.5 | 1.1 | 0.5 | 0.2 |
| 2012 | 99.7 | 0 | 1.8 | 1.7 | 1.7 | 1.2 | 1.0 | 0.6 | 0.3 |
| 2013 | 95.9 | 0 | 2.1 | 1.9 | 1.8 | 1.5 | 1.2 | 0.6 | 0.3 |
| 2014 | 94.0 | 0 | 1.8 | 1.6 | 1.5 | 1.4 | 1.1 | 0.7 | 0.4 |

Figure 16: Statistical summary for daily maximum 8-hour CO Monash 2005 – 2014

## Nitrogen dioxide

Table 16: Statistical summary for daily maximum 1-hour NO2 Monash 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 97.8 | 0 | 0.041 | 0.034 | 0.031 | 0.028 | 0.027 | 0.024 | 0.018 |
| 2006 | 98.4 | 0 | 0.044 | 0.036 | 0.033 | 0.031 | 0.029 | 0.024 | 0.019 |
| 2007 | 97.0 | 0 | 0.039 | 0.037 | 0.035 | 0.030 | 0.028 | 0.023 | 0.018 |
| 2008 | 86.5 | 0 | 0.103 | 0.040 | 0.032 | 0.031 | 0.028 | 0.025 | 0.019 |
| 2009 | 92.6 | 0 | 0.041 | 0.034 | 0.033 | 0.029 | 0.027 | 0.023 | 0.019 |
| 2010 | 89.1 | 0 | 0.037 | 0.029 | 0.028 | 0.025 | 0.023 | 0.021 | 0.017 |
| 2011 | 96.7 | 0 | 0.043 | 0.031 | 0.030 | 0.029 | 0.026 | 0.022 | 0.015 |
| 2012 | 97.5 | 0 | 0.033 | 0.030 | 0.029 | 0.026 | 0.025 | 0.021 | 0.014 |
| 2013 | 97.5 | 0 | 0.037 | 0.031 | 0.030 | 0.027 | 0.025 | 0.021 | 0.014 |
| 2014 | 94.1 | 0 | 0.036 | 0.030 | 0.029 | 0.027 | 0.025 | 0.020 | 0.015 |

Figure 17: Statistical summary for daily maximum 1-hour NO2 Monash 2005 – 2014

Figure 18: Annual average 1-hour NO2 Monash 2005 – 2014

## Ozone

Table 17: Statistical summary for daily maximum 1-hour O3 Monash 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 97.8 | 0 | 0.065 | 0.058 | 0.053 | 0.045 | 0.041 | 0.034 | 0.030 |
| 2006 | 99.7 | 0 | 0.067 | 0.060 | 0.057 | 0.052 | 0.049 | 0.040 | 0.032 |
| 2007 | 95.4 | 0 | 0.075 | 0.064 | 0.062 | 0.057 | 0.052 | 0.043 | 0.032 |
| 2008 | 84.2 | 0 | 0.065 | 0.055 | 0.053 | 0.047 | 0.040 | 0.031 | 0.026 |
| 2009 | 96.4 | 0 | 0.073 | 0.063 | 0.059 | 0.052 | 0.045 | 0.038 | 0.030 |
| 2010 | 86.6 | 0 | 0.051 | 0.048 | 0.046 | 0.042 | 0.037 | 0.033 | 0.030 |
| 2011 | 99.2 | 0 | 0.056 | 0.052 | 0.047 | 0.044 | 0.040 | 0.033 | 0.028 |
| 2012 | 100 | 0 | 0.055 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.062 | 0.051 | 0.049 | 0.045 | 0.041 | 0.035 | 0.029 |
| 2014 | 94.8 | 0 | 0.087 | 0.060 | 0.057 | 0.050 | 0.044 | 0.036 | 0.030 |

Figure 19: Statistical summary for daily maximum 1-hour O3 Monash 2005 – 2014

Table 18: Statistical summary for daily maximum 1-hour O3 Civic 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 85.5 | 0 | 0.070 | 0.061 | 0.051 | 0.042 | 0.038 | 0.032 | 0.028 |
| 2006 | 95.5 | 3 | 0.252 | 0.084 | 0.060 | 0.049 | 0.043 | 0.034 | 0.027 |
| 2007 | 91.5 | 1 | 0.112 | 0.057 | 0.050 | 0.044 | 0.040 | 0.032 | 0.026 |
| 2008 | 91.4 | 0 | 0.052 | 0.050 | 0.044 | 0.039 | 0.034 | 0.028 | 0.023 |
| 2009 | 97.8 | 0 | 0.060 | 0.055 | 0.052 | 0.044 | 0.040 | 0.031 | 0.024 |
| 2010 | 99.2 | 0 | 0.058 | 0.050 | 0.048 | 0.040 | 0.036 | 0.029 | 0.025 |
| 2011 | 96.4 | 0 | 0.052 | 0.046 | 0.045 | 0.041 | 0.036 | 0.030 | 0.026 |
| 2012 | 100 | 0 | 0.053 | 0.041 | 0.038 | 0.034 | 0.030 | 0.024 | 0.020 |
| 2013 | 92.1 | 0 | 0.060 | 0.043 | 0.041 | 0.036 | 0.032 | 0.028 | 0.024 |
| 2014 | 94.0 | 0 | 0.060 | 0.050 | 0.046 | 0.039 | 0.036 | 0.028 | 0.022 |

Figure 20: Statistical summary for daily maximum 1-hour O3 Civic 2005 – 2014

Table 19: Statistical summary for daily maximum 4-hour O3 Monash 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 97.5 | 0 | 0.062 | 0.054 | 0.049 | 0.044 | 0.039 | 0.033 | 0.029 |
| 2006 | 99.7 | 0 | 0.061 | 0.056 | 0.055 | 0.050 | 0.046 | 0.038 | 0.031 |
| 2007 | 100 | 0 | 0.072 | 0.061 | 0.059 | 0.054 | 0.050 | 0.040 | 0.032 |
| 2008 | 84.2 | 0 | 0.061 | 0.052 | 0.049 | 0.045 | 0.038 | 0.030 | 0.025 |
| 2009 | 96.2 | 0 | 0.068 | 0.058 | 0.056 | 0.048 | 0.044 | 0.036 | 0.029 |
| 2010 | 86.6 | 0 | 0.049 | 0.046 | 0.043 | 0.040 | 0.037 | 0.032 | 0.029 |
| 2011 | 98.9 | 0 | 0.054 | 0.048 | 0.044 | 0.041 | 0.038 | 0.032 | 0.027 |
| 2012 | 99.7 | 0 | 0.052 | 0.048 | 0.046 | 0.043 | 0.040 | 0.034 | 0.029 |
| 2013 | 97.8 | 0 | 0.059 | 0.048 | 0.047 | 0.042 | 0.039 | 0.033 | 0.028 |
| 2014 | 94.8 | 0 | 0.060 | 0.055 | 0.052 | 0.046 | 0.042 | 0.034 | 0.029 |

Figure 21: Statistical summary for daily maximum 4-hour O3 Monash 2005 – 2014

Table 20: Statistical summary for daily maximum 4-hour O3 Civic 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 85.5 | 0 | 0.061 | 0.054 | 0.047 | 0.040 | 0.036 | 0.031 | 0.026 |
| 2006 | 95.5 | 1 | 0.145 | 0.066 | 0.053 | 0.045 | 0.040 | 0.032 | 0.026 |
| 2007 | 91.5 | 1 | 0.097 | 0.052 | 0.046 | 0.040 | 0.037 | 0.030 | 0.025 |
| 2008 | 91.4 | 0 | 0.051 | 0.047 | 0.039 | 0.036 | 0.033 | 0.027 | 0.022 |
| 2009 | 97.8 | 0 | 0.059 | 0.049 | 0.047 | 0.041 | 0.037 | 0.030 | 0.023 |
| 2010 | 99.2 | 0 | 0.056 | 0.047 | 0.044 | 0.037 | 0.034 | 0.028 | 0.024 |
| 2011 | 96.4 | 0 | 0.050 | 0.044 | 0.041 | 0.038 | 0.035 | 0.029 | 0.025 |
| 2012 | 100 | 0 | 0.042 | 0.037 | 0.036 | 0.032 | 0.028 | 0.023 | 0.019 |
| 2013 | 91.8 | 0 | 0.057 | 0.040 | 0.038 | 0.034 | 0.030 | 0.027 | 0.023 |
| 2014 | 94.0 | 0 | 0.047 | 0.045 | 0.040 | 0.036 | 0.034 | 0.026 | 0.020 |

Figure 22: Statistical summary for daily maximum 4-hour O3 Civic 2005 – 2014

## PM10

Table 21: Statistical summary for daily maximum 24-hour PM10 Monash 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 99.7 | 3 | 52.0 | 48.2 | 46.0 | 33.8 | 28.5 | 20.7 | 14.7 |
| 2005 | 97.5 | 10 | 98.8 | 57.6 | 52.7 | 37.3 | 31.0 | 21.2 | 14.5 |
| 2006 | 83.8 | 4 | 55.2 | 51.0 | 44.9 | 33.9 | 28.3 | 22.7 | 16.9 |
| 2007 | 99.7 | 5 | 117.7 | 61.8 | 42.5 | 35.3 | 28.0 | 21.0 | 14.9 |
| 2008 | 82 | 3 | 96.6 | 45.8 | 35.7 | 29.9 | 26.6 | 20.1 | 14.8 |
| 2009 | 42.3 | 9 | 210.0 | 116.0 | 62.4 | 50.5 | 37.7 | 25.5 | 15.2 |
| 2010 | 95.4 | 0 | 48.4 | 35.6 | 27.4 | 23.5 | 20.2 | 14.7 | 10.0 |
| 2011 | 99.2 | 0 | 40.0 | 33.7 | 30.3 | 22.8 | 18.6 | 13.2 | 8.7 |
| 2012 | 98.6 | 0 | 41.0 | 24.2 | 21.8 | 19.7 | 17.4 | 13.7 | 9.7 |
| 2013 | 95.6 | 0 | 43.5 | 29.1 | 25.1 | 20.2 | 16.8 | 13.1 | 8.9 |
| 2014 | 97.8 | 0 | 39.3 | 27.1 | 23.1 | 19.1 | 16.4 | 12.9 | 9.6 |

Figure 23: Statistical summary for daily maximum 24-hour PM10 Monash 2005 – 2014

Note: 2009 data has not been included in Figure 23 as the percentile data has been skewed because of insufficient data in Q1 and Q2 (zero and twenty five percent respectively) and the extreme readings associated with the dust storm which affected most of eastern Australia on 22 and 23 September, 2009.

Table 22: Statistical summary for daily maximum 24-hour PM10 Civic 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 9.6 | 1 | 50.64 | 47.2 | 43.8 | 34.8 | 27.5 | 19.5 | 12.7 |
| 2006 | 13.2 | 2 | 70.8 | 61.2 | 51.5 | 46.5 | 35.1 | 26.0 | 17.6 |
| 2007 | 13.2 | 1 | 50.9 | 48.7 | 46.5 | 42.7 | 31.4 | 20.1 | 13.8 |
| 2008 | 12.0 | 1 | 53.3 | 42.5 | 31.7 | 26.1 | 24.2 | 17.3 | 11.9 |
| 2009 | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a | n/a |
| 2010 | 57.6 | 0 | 23.8 | 19.7 | 17.1 | 14.7 | 13.7 | 11.1 | 8.4 |
| 2011 | 97.0 | 0 | 29.2 | 22.3 | 20.9 | 16.9 | 14.4 | 11.0 | 7.9 |
| 2012 | 95.1 | 0 | 49.5 | 22.8 | 20.2 | 17.0 | 14.9 | 12.1 | 8.7 |
| 2013 | 92.9 | 1 | 57.8 | 26.5 | 24.4 | 19.9 | 15.8 | 12.0 | 8.6 |
| 2014 | 95.1 | 0 | 31.4 | 24.2 | 22.1 | 17.7 | 15.1 | 12.6 | 9.3 |

Figure 24: Statistical summary for daily maximum 24-hour PM10 Civic 2005 – 2014

Note:  No PM10 monitoring was conducted at Civic in 2009.

## PM2.5

Table 23: Statistical summary for daily maximum 24-hour PM2.5 Monash 2005 – 2014

| Year | Data Recovery (%) | No. of Exceedences (days) | Max conc. (ppm) | 99th percentile (ppm) | 98th percentile (ppm) | 95th percentile (ppm) | 90th percentile (ppm) | 75th percentile (ppm) | 50th percentile (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2005 | 73.6 | 14 | 38.6 | 31.4 | 29.3 | 25.0 | 20.7 | 9.0 | 4.9 |
| 2006 | 83.3 | 20 | 46.9 | 35.6 | 33.3 | 27.8 | 15.6 | 8.7 | 5.8 |
| 2007 | 58.1 | 8 | 45.7 | 27.8 | 27.6 | 20.9 | 15.7 | 8.8 | 5.4 |
| 2008 | 45.4 | 6 | 30.7 | 28.0 | 25.7 | 23.5 | 19.7 | 12.4 | 6.3 |
| 2009 | 64.5 | 2 | 33.5 | 23.0 | 20.0 | 14.6 | 12.2 | 7.6 | 5.0 |
| 2010 | 95.1 | 2 | 52.4 | 22.1 | 20.9 | 17.4 | 14.3 | 7.8 | 4.4 |
| 2011 | 92.1 | 4 | 32.8 | 25.6 | 22.9 | 20.0 | 12.5 | 7.0 | 4.5 |
| 2012 | 95.1 | 3 | 29.2 | 23.8 | 19.8 | 16.5 | 13.2 | 8.3 | 5.0 |
| 2013 | 98.6 | 6 | 38.4 | 30.5 | 22.7 | 19.2 | 12.9 | 8.1 | 5.2 |
| 2014 | 87.7 | 4 | 31.5 | 25.7 | 21.6 | 18.7 | 14.4 | 8.6 | 5.6 |

Figure 25: Statistical summary for daily maximum 24-hour PM2.5 Monash 2005 – 2014

Figure 26: Annual average 24-hour PM2.5 Monash 2005 - 2014